## Slide 1
Control Theory
EEEN 40010
Electronic, Electrical and Communications Engineering
Dr Paul Curran
Room 145, Engineering and Materials’ Science Centre.
paul.curran@ucd.ie
+353-1-7161846

## Slide 2
Before we begin …
To reduce workload I propose to amend the assessment to this module from that described in the module descriptor, eliminating one component of the assessment, namely the homework. Assessment will rather be based upon four graded laboratories and the reporting thereof, accounting for 15% each and one open-book end of semester examination accounting for 40% This examination will take place during the reading week.
Control Theory
EEEN 40010

## Slide 3
The official assessment will continue to refer to a third assessment component. This fictional component will have a grade assigned which will be determined by appropriate weighting of the grades for laboratories and examination.
Grading is based on “grade steps”. There are 21 grade steps between NG and A+. Work on a particular task earns a certain number of grade steps (fractional grade steps being permitted). The grade for the task is determined by adding the number of grade steps earned, rounding up to the nearest integer and then counting up that number of grade steps from NG.
Control Theory
EEEN 40010

## Slide 4: Overview of Topics
Mathematical background and problem statement.
Dominant pole placement via root locus.
Basic loop shaping.
Linear state feedback and observers.
Digital control.

## Slide 5
Section 0 – Mathematical background and problem statement
Section: 0
Background
Modelling
From models to linear constant coefficient differential equations
Workload:

## Slide 6
Models
Section: 0
In order to obtain scientific predictions of system behaviour one must have a set of mathematical equations which approximately describe this behaviour. You will probably never have a set of equations which exactly describe the behaviour.
Such a set of equations is called a model of the system. Fundamental sciences (such as physics and chemistry) are concerned with finding such models.
Background

## Slide 7
Models
Section: 0
There are two aspects to the problem of finding a model for the behaviour of a system. The first aspect is theoretical. Basic science must suggest the mathematical form that such a model should take. Usually this is subject to a large number of assumptions so it comes with a strong caveat. The first theoretical model will contain within it a number of parameters (such as mass, resistance, etc.). The second aspect is experimental. By performing suitable experiments values for these parameters must be chosen, ideally to give the closest possible fit between the predicted and actual behaviour of the system. In practice these two sub-problems may be (and commonly are) combined into one.
Background

## Slide 8
Models: Example 1
Section: 0
Consider for example the simple gravity pendulum.
Background
Assume the rod to be sufficiently stiff that it does not bow. Assume the mass of the bobbin to be much larger than the rest of the mass of the system. Assume the surroundings and mounting to be still and not subject to buffeting, tremor, etc. Assume a very simple friction model.

## Slide 9
Section: 0
This illustrates an important general fact. We make a large number of assumptions straight away. For example we assume also that the mass of the bobbin is constant. Of course this is false. Surfaces tarnish and joints (such as the mounting joint) wear. In the long run the system performance will degrade. This may be a gradual process or it may be a rather sudden one where some component breaks. But if our interest is in how the system behaves before it breaks and if we only consider a short timeframe then the assumption is usually justified.
Background
Models: Example 1

## Slide 10
Section: 0
The simple gravity pendulum may be analysed by employing basic mechanics. There are at least three approaches which may be taken: force and linear momentum; torque and angular momentum; energy and dissipation. Of course we are entirely ignoring a host of other physical mechanisms such as acoustics and thermodynamics. Again this is typical. We usually determine what are the dominant physical mechanisms involved and just model those. This leads to an approximate model, but indeed there is no other type of model.
Background
Models: Example 1

## Slide 11
Section: 1
Introduction
Performance is approximated by:
We may consider the problem where the bobbin is pulled to a certain angle, allowed to come to rest at this angle and then released. We obtain the following initial conditions:
Models: Example 1

## Slide 12
Section: 0
This illustrates another important and fairly general fact. The mathematical model provided by basic science is commonly an ordinary differential equation (or possibly a system of such equations). Moreover, a differential equation in and of itself does not provide a complete solution of a system problem. One must also specify initial conditions. I should note that the assumption that the angle has come to rest prior to release is plausible but will never be exactly true. There will always be some residual movement.
Background
Models: Example 1

## Slide 13
Section: 1
Introduction
The first aspect has led to the following model:
Parameters m, k, g and l all appear. The second aspect of modelling involves selecting suitable values for these model parameters.
Models: Example 1

## Slide 14
Section: 0
The problem above can be solved in the special case where the friction is absent, i.e. k = 0. The solution dates from 1898 (Helmholtz et al.) and it involves a special function denoted sn which is one of a set of special functions known collectively as Jacobi’s elliptic functions. In the more general case where friction is present, even the relatively simply friction considered here, the situation is less satisfactory from the theoretical perspective.
Background
Models: Example 1

## Slide 15
Section: 0
The pendulum example is very typical in many ways but it is atypical in at least one important way. The external intervention to the system (human or otherwise) amounts to the setting of the initial condition only. Otherwise the system progresses on its own, governed by its own physical laws and disconnected (courtesy of many of our less plausible assumptions) from the rest of the universe.
Background
Models: Example 1

## Slide 16
Section: 0
Consider for example the launch of a rocket. Upward acceleration is provided by the thrust from the main engine(s). This is opposed by gravity and drag. A simple characterisation is:
Background
where m denotes the mass, T denotes thrust, Cd denotes the drag coefficient, A denotes the transverse cross-sectional area, h denotes the altitude, r denotes air density and g denotes gravitational acceleration.
Models: Example 2

## Slide 17
Section: 0
This apparently somewhat simple equation hides numerous issues. Gravitational acceleration depends upon the inverse square law, hence g decreases as h increases. Air density decreases with altitude but the rate of decrease depends upon pressure, temperature, humidity and other factors. Thrust depends on throttle setting and on air density among other things. Even with a fixed throttle setting it will generally decrease with altitude.
Background
Models: Example 2

## Slide 18
Section: 0
A significant portion of the mass of a rocket is comprised of the propellant (often called the fuel). Propellant is exhausted (i.e. expelled through the main engine) during launch. It follows that the mass decreases significantly with time. The formula for the drag is approximate at the best of times. To employ it one must recognise that the drag coefficient will not be constant. At the very least a significant change takes place at trans-sonic speeds.
Background
Models: Example 2

## Slide 19
Section: 0
The definition of trans-sonic speeds (i.e. speeds neighbouring the speed of sound) depends upon the speed of sound itself, and this also depends upon air density, among other factors. The cross-sectional area A typically does not remain constant because of staging. At some point a stage of the launch comes to a close and a part of the rocket is jettisoned. As well as involving a rather sudden drop in mass this can also involve a sudden change in cross-sectional area.
Background
Models: Example 2

## Slide 20
Section: 0
So every “parameter” in this equation is actually changing and many change with altitude h. Some of these changes are rather unpredictable. The air density depends for example on the moisture content of the air currently surrounding the rocket and of course we cannot know that in advance for every point along the trajectory. Moreover we have not modelled unpredictable disturbances, due to wind for example, at all.
Background
Models: Example 2

## Slide 21
Section: 0
There is one way in which this example is more typical of engineering systems than the pendulum. External intervention in the form of the thrust affects the rocket throughout the flight. We as humans do not simply set the initial conditions and then let the system go. We actually fly the craft and the setting of the thrust (usually by adjustment of the throttle) is one of our principle mechanisms for controlling that flight.
Background
Models: Example 2

## Slide 22
Section: 0
Of course an actual rocket is more complicated still since it is not a point mass. It is an object with actual physical dimensions. In terms of mechanics it can rotate or spin. Rotation about certain axes can be catastrophic. The message is somewhat dispiriting: real things are messy and difficult. We cannot exactly model them and we cannot analytically solve the equations which even approximate their behaviour.
Background
Models: Example 2

## Slide 23
Section: 0
Consider for example an elementary one-tank liquid level system. Assuming a high pressure, turbulent output flow, the system may be characterised as follows :
Background
where Qin denotes the controlled (i.e. pumped) input flow, Qout denotes the output flow, A is the tank cross-sectional area (assumed constant w.r.t. height), Ad denotes the outlet pipe cross-sectional area, Cd denotes a coefficient characterising the outlet.
Models: Example 3

## Slide 24
Section: 0
Background
represents yet another equation which is difficult to solve in general. A critical idea is that there is likely to be some desired value hr of the liquid level. This might be called the rated value or the operating point. What value must the input flow attain in order for the liquid level to remain at the rated value? Well if h is unchanging at the value hr then:
Models: Example 3

## Slide 25
Section: 0
Background
Now suppose that the liquid level is close to the rated value. It may have been disturbed from it for some unforeseen reason. Introduce offset variables (or signal values)
Models: Example 3

## Slide 26
Section: 0
Background
Since the liquid level is assumed close to the rated value it follows that the ratio is small. It is therefore possible (by employing the Maclaurin expansion) to deduce that:
Models: Example 3

## Slide 27
Section: 0
Background
This simplifies to:
This is a far simpler equation in part because it is linear. The parameter a also does not change with time, so in fact the equation is linear and has constant coefficients.
Models: Example 3

## Slide 28
Section: 0
Now of course this equation only approximately describes the performance of the liquid-level system provided it operates close to the rated level. There are some rather deep theoretical results relating the behaviour of the system close to the rated value and the behaviour of the approximate linear system. But these results only prove what is intuitively obvious, that the behaviour of the actual level h(t) is quantitatively the same as .
Background
Models: Example 3

## Slide 29
Section: 0
It is possible to rather satisfactorily analyse the “offset” system, i.e. the system described by:
Background
Towards this end we note a consequence of linearity. Suppose that a particular solution of the equation is
Consider the associated homogeneous equation:
Models: Example 3

## Slide 30
Section: 0
Background
Suppose that a particular solution of the homogeneous equation is
It follows that another solution of the equation is:
Moreover this is the general solution of the equation for if and are two solutions of the equation then is a solution of the homogeneous equation. This is true of linear equations in general.
Models: Example 3

## Slide 31
Section: 0
Background
Important observation #1:
The general solution of a linear ordinary differential equation equals the sum of a particular solution and a solution of the associated homogeneous equation.
Models: Example 3

## Slide 32
Section: 0
Background
General solutions of the associated homogeneous equations are readily come by. For the present example the homogeneous equation is:
The key idea is to recognise the pivotal role of the exponential function. Specifically look for a solution of the form
Models: Example 3

## Slide 33
Section: 0
Background
So a solution of the homogeneous equation is
for arbitrary choice of constant A. This solution is of course an exponential function. The exponent is –a. The homogeneous equation
may be written as:
where the symbol D denotes the operation of differentiation.
Models: Example 3

## Slide 34
Section: 0
Background
A key observation is that there is, associated with the homogeneous equation, a polynomial, namely the polynomial:
which is obtained by formally replacing the differentiation operation by the symbol D and subsequently replacing the symbol D by the symbol s. The important point is that the root of this polynomial, namely –a is the exponent of the exponential appearing in the general solution to the homogeneous equation.
Models: Example 3

## Slide 35
Section: 0
Background
Important observation #2:
The general solution of a linear, constant coefficient, homogeneous, ordinary differential equation almost always equals a sum of exponentials. Moreover the exponents of the exponentials appearing in this sum are the roots of a polynomial which may be acquired from the equation itself in an elementary and systematic manner.
What is true in the case of this special linear, constant-coefficient equation is true in general.
Models: Example 3

## Slide 36
Section: 0
Background
Now there is a very clever and rather general idea for determining a particular solution of a linear equation when a solution to the associated homogeneous equation is known. It is called the method of variation of parameters. For the equation
we have the solution to the associated homogenous equation:
The method of variation of parameters suggest looking for a particular solution of the form:
Models: Example 3

## Slide 37
Section: 0
Background
Putting this purported solution into the equation yields:
Models: Example 3

## Slide 38
Section: 0
Background
Without loss of generality we select y(0) = 0. The general solution to the equation becomes:
The associated approximate solution to the liquid-level system is:
provided the offset from the rated value remains small.
Models: Example 3

## Slide 39
Section: 0
Background
In engineering systems we generally control inputs such as qin(t), setting them so that, disturbances and perturbations notwithstanding the system does indeed remain close to the desired or rated value. The assumption that the system operates close to some desired operating point is in general a much safer assumption to make of engineering systems because there exists an entire control infrastructure whose raison d’être is to ensure that this assumption holds. In the electric utility for example a slew of governors cajole the grid frequency to be 50Hz.
Models: Example 3

## Slide 40
Section: 0
Background
The upshot is that linear systems, which are really only approximate descriptions of system performance close to some desired location, actually provide a rather effective and useful set of models for practical engineering systems. Indeed it is broadly accurate to assert that much of engineering is based upon approximate linear models. There is, however, a rather important caveat. The approximate models which emerge in this manner may be linear, but they do not necessarily have constant coefficients. Moreover they also may not be linear.
Models: Example 3

## Slide 41
Section: 0
Background
The correct phrase which should be employed for these approximate models, supposedly valid close to a desired operating point, is first approximation. Although this phrase is employed in western literature it is not employed sufficiently often. In western literature it is far more common to see the phrase linearisation and that is in the rather small percentage of cases where any mention at all is made of the approximation process. More commonly everything is assumed linear from the moment of its introduction.
Models: Example 3

## Slide 42
Section: 0
Background
You will probably have seen this kind of thing with Ohm’s law for example. There are two laws named after Georg Ohm, but one of them, that the voltage across a resistor is proportional to the current flowing through it, is far more common so that relatively few people are aware of the ambiguity. As stated I have in fact misquoted the more famous Ohm’s law. In fact the statement of the law which I have given is preposterous.
Models: Example 3

## Slide 43
Section: 0
Background
To demonstrate suppose I have a 1 kW resistor. If I place 1 V across it then 1 mA of current will flow through it. The electrical power delivered to the device will be 1 mW. This is not a large amount of power. The device will mainly react to this infusion of electrical energy by heating up, but it can easily shed this heat by radiation and conduction to its surroundings. If however I place 1 GV across the device then 1 MA of current will flow through it. The electrical power delivered will be 1x1015 W. This is an immense amount of power, far in excess of what the device can shed in the form of heat lost to its surroundings. Long before I have raised the voltage to this level the device will simply have melted.
Models: Example 3

## Slide 44
Section: 0
Background
Actually the more famous Ohm’s law states that the voltage across a resistor is in direct proportion to the current flowing through it when all other things remain unchanged. It is this rider, commonly and somewhat sloppily omitted, which permits the law meaning, when examples such as the previous slide suggest that it must be nonsense. When I place 1 GV across a 1 kW resistor, or rather when I increase the applied voltage towards this value, I find that I simply cannot remove the resulting thermal energy fast enough. All other things do not remain unchanged. Rather the temperature of the device steadily increases and, strictly speaking, about this situation Ohm’s law has nothing whatsoever to say.
Models: Example 3

## Slide 45
Section: 0
Background
Such serious issues notwithstanding a resistor will commonly be modelled by the linear equation V = RI for some constant value of resistance R. When the modus operandi of modelling is to introduce all elements as linear components or rather to linearise from the outset, then the resulting model will inevitably be linear. Unfortunately the linear model may also be completely invalid. Some systems do not possess first approximations which are linear and these systems are not esoteric, purely academic systems, they are actual real systems which occur in very large numbers of engineering products (in mobile phones for example).
Models: Example 3

## Slide 46
Section: 0
Background
Even if the first approximation is linear it may not be constant-coefficient. In the case of the rocket for example we may have a desired or target trajectory for the flight. By looking for the equations which describe the deviation of the actual trajectory from this target, subject to the assumption that these deviations are small (an assumption known in the field of electronics as the small signal approximation) we may be able to find an approximate set of linear equations describing this deviation. However, many components of the “true” equations depend upon altitude, i.e. upon the current location on the trajectory, and therefore upon time which parameterises this trajectory. It follows that the first approximation may be linear, but it varies with time.
Models: Example 3

## Slide 47
Section: 0
We have solved the first approximation equations for the liquid-level system.
Background
For some special cases of the forcing term we may demonstrate another very powerful method of solution.
Models: Example 3

## Slide 48
Section: 0
Consider the special case:
Background
assuming:
For any complex number s for which integrals converge:
Models: Example 3

## Slide 49
Section: 0
I note that if the function is uniformly bounded in modulus for t ≥ 0 then this limit equation holds for every complex number s for which
Background
Models: Example 3

## Slide 50
Section: 0
We note that the polynomial s+a has emerged. It is possible, using the partial fraction expansion to rewrite as
Background
Models: Example 3

## Slide 51
Section: 0
Lerch’s cancellation law establishes that:
Background
We have obtained the general solution by a quite ingenious method. This method is called the Laplace transform method.
Models: Example 3

## Slide 52
Section: 0
Background
As it has been applied in the above case the Laplace transform method is based upon five ideas. Firstly we note that if
for any weighting function w(t) chosen such that the integral converges. In general the integral will converge provided the integrand goes to zero sufficiently rapidly. A decaying exponential does indeed converge to zero rapidly so the choice of weighting function exp(-st) is somewhat reasonable.
Models: Example 3

## Slide 53
Section: 0
Background
Since
for any weighting function w(t) chosen such that the integral converges we may observe that it holds, not for a single weighting function, but for a whole class of weighting functions. If all of the individual integrals converge then
Models: Example 3

## Slide 54
Section: 0
Background
The next idea is to process the first of these integrals by using the method of integration known as integration by parts. This is the inverse of the product rule of differentiation being derived by combining the product rule with the fundamental theorem of calculus.
For a general weighting function w(t) this formula will be messy. Is there a choice of the weighting function which will simplify it?
Models: Example 3

## Slide 55
Section: 0
Background
Firstly I should note that the weighting function has been chosen so that, among other things, the integral
converges. A necessary condition for this convergence is that the integrand converge to zero, i.e.
Models: Example 3

## Slide 56
Section: 0
Background
Now it was noted from their first introduction that the exponential functions possess a particularly notable property from the perspective of the calculus
for any exponent l, real or complex. It has taken us as a specie a long time to fully appreciate the consequences of this simple observation, and indeed it may well be that we have yet to fully appreciate them. For the present we may simply note the fact, but there are now some very deep explanations and interpretations of it.
Models: Example 3

## Slide 57
Section: 0
Background
If the weighting function is chosen as an exponential function, exp(lt), then
for any exponent l, real or complex. Since we want certain integrals to converge we feel that the weighting functions chosen should converge to zero reasonably rapidly. If
Note: I denote the square root of -1 by j not i.
Models: Example 3

## Slide 58
Section: 0
Background
For every real number t, the complex number, exp(jwt) has modulus equal to unity. Accordingly it does not converge to zero. It follows that
converges to zero only if the real part, s, of the exponent l is negative. We deduce that if we select for our class of weighting functions the exponential functions exp(lt) then we should restrict the exponents l so that Re(l) = s < 0. It has been found convenient to write l = -s and restrict complex s to have positive real part instead.
Models: Example 3

## Slide 59
Section: 0
Background
We deduce that a potentially good choice of the class of weighting functions is to extract them from the set of exponential functions, exp(-st), where the complex numbers s have positive real part. We may indeed have to restrict the class of weighting functions further but this much at least we elect to do. With this choice
Models: Example 3

## Slide 60
Section: 0
Background
The next step is simple:
where it seems we should further restrict s so that it does not equal –a. The final steps depend upon the nature of the input Qin(t) and we shall not take them here. A few points may be made however. Evidently the integral
plays a significant role. Of course the value of the integral depends on s, i.e. it is a function of s.
Models: Example 3

## Slide 61
Section: 0
Background
Recognising this we write:
Although it is not quite correct to do so it is common enough to call this function Qin(s) the Laplace transform of the input . So we obtain
Models: Example 3

## Slide 62
Section: 0
Background
Another key idea in the Laplace transform method is based upon the very simple observation that, should s be chosen such that the integral converges then
Models: Example 3

## Slide 63
Section: 0
Background
If it is possible to find f(t) such that
Finally Lerch’s cancellation law possibly gives (there are a few conditions to check):
Models: Example 3

## Slide 64
Section: 0
Background
Consider a preliminary model of a vehicle suspension system.
Models: Example 4
f = road disturbance

## Slide 65
Section: 0
Background
Evidently this is a highly simplified model of what is usually referred to as a quarter car. The spring models both the suspension spring and the tyre. The damper models the shock absorber. A shock absorber commonly acts like a spring-damper combination but the spring-like behaviour has again been absorbed into the one spring in the model. The mass equals a quarter of the vehicle mass at least. The deflection f represents the undulation of the road surface above a fixed reference. Linear models are employed for the spring and damper, which as noted is unrealistic.
Models: Example 4

## Slide 66
Section: 0
Background
The equation obtained is essentially identical to that obtained for the approximate model of the pendulum except for the presence of a forcing term, namely the road disturbance. This illustrates a very important point: mathematics is actually universal. The same mathematical model can describe an abundance of physically quite distinct systems. The model is a linear, constant-coefficient ordinary differential equation.
Models: Example 4

## Slide 67
Section: 0
Background
In reality the vehicle travels along the road so that the road disturbance f is a function of position along the road. Given the velocity along the road of the vehicle however we may find the position of the vehicle at any given time so that the road disturbance can be translated into a function of time. In the model presented we allow our co-ordinate system to travel along the road with the vehicle. Accordingly the vehicle is motionless relative to the horizontal of this moving co-ordinate system and the actual movement is manifested in the model by a time varying road disturbance.
Models: Example 4

## Slide 68
Section: 0
Background
A valuable feature if linearity is as follows. Suppose the road disturbance f can be expressed as a sum of several disturbances. There might for example be a sudden jump corresponding to a seam or pothole, there might be a smooth undulation, there might be a rather jittery, possibly random component representing the bumpy nature of the surface of a real road. Accordingly:
Models: Example 4

## Slide 69
Section: 0
Background
It follows that the general solution of the equation is given by:
Models: Example 4
where x0(t) is a solution to the associated homogenous equation and xi(t) is a particular solution to the non-homogeneous equation:

## Slide 70
Section: 0
Background
Important point #3
We can simplify the problem of finding the general response of a forced linear system. It is equal to the response to the homogeneous equation (i.e. the unforced system) added to the particular response to each individual component of the forcing term.
Models: Example 4

## Slide 71
Section: 0
Background
This observation leads to a significant problem. Given a general input or forcing term (i.e. road disturbance in this case) is there some obvious way of identifying the “components” of this input? Of course the “components” should represent something that is physically important (a seam for example in the present case) but, if possible it would seem reasonable to try also to select the components so that the problem of finding the associated component of the particular system response (xi(t) in this case) is simplified.
Models: Example 4

## Slide 72
Section: 0
Background
Although again there are very deep explanations and interpretations available we may simply observe one mathematical “component” for which the associated particular solution may be rather easily found. Consider the equation for the special input cos(wt). We seek a particular solution to the equation:
Models: Example 4

## Slide 73
Section: 0
Background
Suppose we simply guess that there may be a solution of the form Acos(wt+f). Then
Models: Example 4
This equation is a bit tedious to work with, however there is a very elegant idea which greatly simplifies the task. We must recall two wonderful formulae:

## Slide 74
Section: 0
Background
Now the idea is to replace all of the trigonometric functions by their expansions in terms of complex exponential functions:
Models: Example 4
This looks worse than before but I can rearrange:

## Slide 75
Section: 0
Background
Models: Example 4
Let:

## Slide 76
Section: 0
Background
Models: Example 4
The equation becomes:
where z1 and z2 are certain fixed complex numbers and where this equation must hold for all times t. Evidently the left hand side changes with time t if z1 is non-zero. The right hand side of course is fixed. From this incompatibility I deduce that z1 and therefore also z2 must both be zero. It is reasonably clear that

## Slide 77
Section: 0
Background
Models: Example 4
It follows that the equation becomes:

## Slide 78
Section: 0
Background
Models: Example 4
So the particular solution when the forcing term is a sinusoid cos(wt) (i.e. a unit amplitude co-sinusoid of radian frequency w rad/sec) is also a co-sinusoid of radian frequency w rad/sec, namely Acos(wt+f). The amplitude A and phase f are described by the equation:
An elegant and fairly elementary solution to the problem is obtained provided we employ complex numbers.

## Slide 79
Section: 0
Background
Models: Example 4
For a given frequency w and given system parameters m, m and k the right hand side is just a complex number. The amplitude A of the sinusoidal particular solution is then obtained as the modulus of this complex number. The phase f of the sinusoidal particular solution is likewise obtained as an argument of this complex number. All of this occurs more generally.

## Slide 80
Section: 0
Background
Models: Example 4
Important observation #4:
A particular solution to a linear, constant-coefficient ordinary differential equation with a forcing term which is a sinusoid cos(wt) (i.e. a unit amplitude co-sinusoid of radian frequency w rad/sec) is also a co-sinusoid, Acos(wt+f), of radian frequency w rad/sec. The amplitude A and phase f of this particular solution may be obtained by a systematic process directly from the equation.

## Slide 81
Section: 0
Background
Models: Example 4
We find that the amplitude of the particular co-sinusoidal solution varies with the frequency w of the forcing term. At zero frequency (DC) the amplitude is 1. At very large frequencies the amplitude falls towards 0.

## Slide 82
Section: 0
Background
Models: Example 4
We may plot the amplitude vs. frequency. In the plot I have taken k = 1, m = 1 and m = 0.1.
The plot reveals the important phenomenon of resonance.

## Slide 83
Section: 0
Background
Models: Example 4
The plot on the previous slide is a special case of an amplitude response plot in turn a part of the frequency response. We see that at a frequency of 1 rad/sec the amplitude of the response of the suspension system is 10, whereas that of the input component was 1. The system amplifies a 1 rad frequency tenfold. This is the phenomenon of resonance. All structures have resonant frequencies, i.e. frequencies which are amplified by the structure. Resonance is the curse of bridges, tall buildings and vehicle chasses and suspension systems.

## Slide 84
Section: 0
Background
Models: Example 4
We see also that at a reasonably high frequency the amplitude of the response of the suspension system is almost zero, whereas that of the input component was 1. The system attenuates high frequencies. This is ubiquitous. No systems can react infinitely rapidly. Accordingly no systems can react at all to infinitely high frequencies.

## Slide 85
Section: 0
Background
Models: Example 4
Of course the input to a system, and in particular the input to the suspension system of the present example will not be a co-sinusoid. The sinusoids are a very useful set of mathematical functions, but it is false to suggest that they actually exist as real signals, for example as an actual road disturbance. For one sinusoids are periodic and therefore go on forever. Roads of course do not. Should we care that the system has a resonance at 10 rad/sec if the input to the system can never be a sinusoid at all, let alone a sinusoid of this particular frequency?

## Slide 86
Section: 0
Background
Models: Example 4
The answer is unequivocally that it does indeed matter. Although an input (the road disturbance in this case) may not be a sinusoid it transpires that it may contain a component which is a sinusoid. By way of illustration consider the following signal:
It is apparent that this signal is not a sinusoid.

## Slide 87
Section: 0
Background
Models: Example 4
It is a standard application of contour integration to establish that:
The integration is achieved by considering the contour integral:
Two different contours are employed, one for t > 0 and one for t < 0. Subsequently Cauchy’s residue theorem is applied. The calculation for t = 0 is more straightforward and may be achieved directly.

## Slide 88
Section: 0
Background
Models: Example 4
The formula:
establishes that the signal f(t), although it is not even periodic, may in fact be expressed as a “sum” of co-sinusoids of all non-negative frequencies. Granted the “sum” is a bit unusual, not only is it not a finite sum, it is not even a countable infinite sum. In fact it is an uncountable infinite sum, although we do not call such things sums, we call them integrals.

## Slide 89
Section: 0
Background
Models: Example 4
In fact a very large number of real functions can be written as:
for a suitable associated function F(jw). This function is called the Fourier transform of the function f(t). The two expansions of this formula establish that the real function f(t) is really some kind of superposition of the complex exponential functions exp(jwt) or alternatively the co-sinusoids.

## Slide 90
Section: 0
Background
Models: Example 4
Important observation #5:
Although a real signal will not be periodic it may commonly be expressed as a “sum” of sinusoids. Accordingly the signal may nonetheless have a component which is a sinusoid at a certain frequency.

## Slide 91
Section: 0
Background
Models: Example 4
The equation:
is interpreted as describing the frequency content or spectrum of the signal f(t). In short, if the Fourier transform F(jw) is not zero at the frequency w then we interpret this as saying that some of the energy of the signal takes the form of a component of the signal which is equal to a sinusoid of frequency w. Indeed the modulus of F(jw) expresses the weighting of or degree to which this frequency is present.

## Slide 92
Section: 0
Background
Models: Example 4
In the case of the suspension system with a resonance at 10 rad/sec it will not matter that the road disturbance cannot be a sinusoid. If the spectrum of the road disturbance indicates that there is a significant component of that disturbance at frequencies at or close to 10 rad/sec then this component of the disturbance will be amplified by the system. In short we actually experience resonance occurring in real systems notwithstanding that sinusoids do not really exist.

## Slide 93
Section: 0
Background
Now recall the model of the suspension system.
Models: Example 4
f = road disturbance

## Slide 94
Section: 0
Background
Models: Example 4
Suppose we attempt to solve this equation by the two methods of solution considered above in the case of the liquid-level system. To be specific take parameter values m = 1, k = 1 and m = 0.1 as above.

## Slide 95
Section: 0
Background
Models: Example 4
The first method requires firstly that we solve the associated homogeneous equation. I will also impose the known initial conditions:
As the system is linear, constant-coefficient we look for a solution of the form exp(bt) , i.e.

## Slide 96
Section: 0
Background
Models: Example 4
A solution of this form exists provided the exponent b is a root of the polynomial:
This polynomial has two complex roots which are of course conjugates:
By linearity we obtain a general solution to the homogeneous equation:

## Slide 97
Section: 0
Background
Models: Example 4
There are two arbitrary coefficients in this general solution formula. This is sufficient to permit us to tailor it to meet any given initial conditions:
which is solvable if the determinant of the matrix is non-zero, i.e. if b1 and b2 are not equal.

## Slide 98
Section: 0
Background
Models: Example 4
Now we require a particular solution satisfying zero initial conditions and we apply the method of variation of parameters:

## Slide 99
Section: 0
Background
Models: Example 4

## Slide 100
Section: 0
Background
Models: Example 4
This equation does not uniquely define the functions c1 and c2. It seems that the method has failed. The additional clever idea is to constrain these functions. In this case we require:

## Slide 101
Section: 0
Background
Models: Example 4
The determinant appearing here, is given a special name. It is called the Wronskian.

## Slide 102
Section: 0
Background
Models: Example 4
This is the second time that the method of variation of parameters has given a solution of this form. In fact this is quite general.
Important fact #5
In general the particular solution of linear constant coefficient with forcing term f(t) having zero initial conditions takes the form:

## Slide 103
Section: 0
Background
Models: Example 4
One view of the Laplace transform method is that it comprises an often rather efficient procedure for calculating the function h appearing in this general formula for the particular solution.

## Slide 104
Section: 0
Background
Models: Example 4
Now consider the Laplace transform method:
Apply integration by parts:

## Slide 105
Section: 0
Background
Models: Example 4
where it assumed s chosen such that all of the integrals converge and therefore all of the integrands converge to zero. Let

## Slide 106
Section: 0
Background
Models: Example 4

## Slide 107
Section: 0
Background
Models: Example 4
The quantity multiplying the function F(s), namely
has substantially appeared above, albeit with the complex variable s replaced by jw. It appeared in the formula:
for the amplitude and phase of the particular co-sinusoidal solution in the event that the forcing term was a unit amplitude co-sinusoid of radian frequency w (rad/sec).

## Slide 108
Section: 0
Background
Models: Example 4

## Slide 109
Section: 0
Background
Models:
There are significant generalisations of almost everything which has been said above, particularly in the case of example 4. This module is largely about solving the equations which comprise the first approximation close to an operating point, assuming that this first approximation is linear and constant-coefficient. We will consider also some deeper explanations and interpretations of the ideas considered above.

## Slide 110
Laplace Transform
Section: 1
Block Diagrams
1749-1827
Given a function f of a continuous variable t let
for those complex s for which the integral converges.
The nature of the integral is justified by the previous discussion of the Laplace transform method, with a single caveat, the lower bound of the integral is 0- rather than 0. This means that the lower bound is actually –e as e approaches 0.

## Slide 111
Laplace Transform
Section: 1
Block Diagrams
We call this rather odd lower bound the limit as t approaches zero from below. In my previous discussion we adopted the much more straightforward lower bound of 0. The reason for this rather technical discrepancy is to ensure that the Laplace transform will work correctly when dealing with a rather unusual mathematical object known variously as the Dirac delta function or ideal impulse. I will have no need to deal with this issue although the majority of you have met it before.

## Slide 112
Laplace Transform
Section: 1
Block Diagrams
This integral defines the function F(s) for some s, those for which the integral converges. There are two approaches to dealing with the other values of s. One approach is to not define the function at all at these values. It is fair to say that this is the more common approach in engineering textbooks. Lerch’s cancellation law holds provided the equality holds for a large number of values of s, it does not require that it hold for all values of s.

## Slide 113
Laplace Transform
Section: 1
Block Diagrams
A second approach which I deem far superior defines the function for all values of s. There is a very deep idea in complex analysis which permits “continuation” of the definition of a function of a complex variable from a set of complex numbers to all the complex numbers. The idea is called analytic continuation.

## Slide 114
Laplace Transform
Section: 1
Block Diagrams
Definition 1.1: Given signal f the function, F(s), defined as above for all s for which the integral converges and by analytic continuation for all other s, is called the Laplace Transform of f, denoted L(f).
Analytic continuation is a very deep theoretical concept and sometimes the process of achieving it requires real mastery of the subject. For the signals which we deal with however it is almost trivial.

## Slide 115
Example 5
Section: 1
Definition 1.2: The step function u(t) is given by
Block Diagram
Notes: The integral establishes this result for s in the open right half plane. Analytic continuation extends the result to all s.

## Slide 116
Laplace Transform Properties: 1
Section: 1
This property is called linearity.
Block Diagrams

## Slide 117
Laplace Transform Properties: 2
Section: 1
These are called the shifting properties.
Block Diagrams

## Slide 118
Laplace Transform Properties: 3
Section: 1
This is called the differentiation property. Obviously we assume that the function is suitably differentiable. For the special case n = 1 it asserts that
Block Diagrams

## Slide 119
Final Value Theorem
Section: 1
Block Diagrams
where I assume that both limits exist. Obviously this is a technical result, but we will shortly see that it has very significant application in the area of control theory. The result is essentially a direct consequence of the n = 1 case of the differentiation property.

## Slide 120
Example 6
Section: 1
Block Diagrams

## Slide 121
Solving linear, constant coefficient ODEs
Section:1
Block Diagrams
f(t) is a given input or forcing term. g(t) is the output or response of the system.

## Slide 122
Laplace Transform
Section: 1
Block Diagrams
In the light of the introductory examples I can credibly claim that equations of this kind will model a good number of engineering systems in a particular sense. Specifically they will predict how the offset of the system from its desired operating point evolves with time, subject to the assumption that this offset is initially and remains thereafter suitably small. If the equations predict a growth in the offset then all that really happens is that the system departs from the operating point and therefore leaves the region where the approximate linear, constant-coefficient ODE model is valid.

## Slide 123
Solving linear, constant coefficient ODEs
Section:1
Block Diagrams

## Slide 124
Solving linear, constant coefficient ODEs
Section:1
Block Diagrams

## Slide 125
Laplace Transform
Section: 1
Block Diagrams
The solution (or rather its Laplace transform) emerges as the sum of two component. One, H(s)F(s), depends only on the forcing term, not on the initial conditions. In the previous terminology it is a particular solution. More than that it is a particular solution which has zero initial conditions. My previous division of the solution into a sum of a particular solution and a solution to the homogeneous equation is unsatisfactory because these components are not thereby uniquely defined. We can uniquely define them if we insist that the particular solution should moreover satisfy zero initial conditions and the solution to the homogeneous equation should satisfy the given initial conditions and this I propose to do.

## Slide 126
Laplace Transform
Section: 1
Block Diagrams
The first component is called the forced response. So the forced response is the particular solution which satisfies zero initial conditions. The second component Q(s)/D(s) depends only on the initial conditions and is independent of the forcing term. It is called the free response. Physically it is telling us how the system “shakes off” its initial stored energy. The pendulum equation was unusual because there was no forced response only a free response.

## Slide 127
Laplace Transform
Section: 1
Block Diagrams
This iconic equation tells us something quite remarkable. Viewed in the right way the action of every linear constant-coefficient ODE in terms of how it transforms a forcing term into a forced response is really just the same as the elementary mathematical operation of multiplication. The quantity H(s) appearing in this formula is called the transfer function.

## Slide 128
Example 7
Section: 1
Block Diagrams
A robotic arm is fixed to the shaft of a DC motor and free to rotate in the horizontal plane. We control the input voltage to the motor.

## Slide 129
Section: 1
Block Diagrams
We have to first model the system. Obviously a first attempt is to employ standard models. On the electrical side one of the simplest standard models of a DC motor is as shown. The physical effects modelled are the resistance of the stator wire, the self-inductance of this wire and the back emf generated by the rotor.
Example 7

## Slide 130
Section: 1
Block Diagrams
Of course this electrical model follows the “linear from the outset approach” which I have previously disparaged. I must bear in mind that appropriate values for the various parameters should be chosen for when the motor is close to its desired operating point, including for example its desired temperature. I must recognise that should the device depart significantly from these desired settings then the chosen parameter values will no longer be appropriate and indeed the model may fail. An obvious failure mechanism for example would be saturation of the iron in the core.
Example 7

## Slide 131
Section: 1
Block Diagrams
On the mechanical side we employ substantially the rotational form of Newton’s law (sometimes called Euler’s law).
Here J denotes the moment of inertia of the arm. T is the torque (or moment) applied. This is comprised of two components: the motor torque Tm and the friction torque which we assume proportional to angular velocity. For the motor torque we have the important relationship:
Example 7

## Slide 132
Section: 1
Block Diagrams
We obtain as a result the following set of equations:
Example 7

## Slide 133
Section: 1
Block Diagrams
Or rearranging:
We obtain a linear, constant-coefficient ODE with forcing term v(t), being the voltage input to the motor and response q(t) being the angle of the arm. We may take the Laplace transform of both sides and apply the transform properties, specifically differentiation and linearity.
Example 7

## Slide 134
Section: 1
Block Diagrams
Example 7

## Slide 135
Section: 1
Block Diagrams
Example 7

## Slide 136
Example 7
Section: 1
Block Diagrams
s-domain or block diagram model of DC motor and arm

## Slide 137
Inverse Laplace Transform
Section: 1
Definition 1.6: Given F(s) the function f(t)
satisfying f(t) = 0 for t < 0 and L(f(t)) = F(s)
is called the inverse Laplace transform of F,
denoted L-1(F ).
Block Diagrams

## Slide 138
Inverse Laplace Transform
Section: 1
This slightly subtle definition comes about by a more careful consideration of Lerch’s cancellation law. If
Block Diagrams
for a suitable set of complex numbers s, then
the point being that the cancellation law says nothing about the equality of the signals for t < 0.

## Slide 139
Inverse Laplace Transform
Section: 1
The proof of Lerch’s cancellation law and the basis of the inverse Laplace transform, and indeed the transform itself, is contour integration. For those who have some knowledge of this two contours are chosen, one for t > 0 and one for t < 0. The contours share one section, a line parallel to the imaginary axis but to the right of all of the poles of the function F(s) whose inverse transform is being sought. The complex function F(z)exp(zt) is integrated around the appropriate contour by applying Cauchy’s residue theorem.
Block Diagrams

## Slide 140
Inverse Laplace Transform
Section: 1
The method partially described for inversion only applies if there actually is a line parallel to the imaginary axis to the right of all of the poles of F(s). Actually we require even more, the function must be analytic in the region of the complex plane lying to the right of this line. It follows that the function F(s) must be analytic in a region Re(s) > s of the complex plane. Although the mathematics is a little tricky this requirement also explains the somewhat subtle analytic continuation-based definition of the Laplace transform. For those interested (and I can think of two who might be) I am happy to provide details in my office.
Block Diagrams

## Slide 141
Inverse Laplace Transform
Section: 1
In general the problem of determining the inverse Laplace transform is a somewhat sophisticated mathematical problem. There is a special case, actually the only case that a great many engineers ever need to consider, where the problem becomes far more routine. This is the case where the function F(s) whose inverse Laplace transform is sought is a rational polynomial, i.e. a ratio of two polynomials.
Block Diagrams

## Slide 142
Partial Fraction Expansion
Section: 1
Block Diagrams

## Slide 143
Inverse Laplace Transform
Section: 1
Block Diagrams

## Slide 144
Inverse Laplace Transform
Section: 1
The upshot is that when F(s) is a rational polynomial we may express it in a particular form (the partial fraction expansion) and we then have available a completely general inversion formula.
Block Diagrams