## Slide 1
Control Systems
Stage 4: Electrical, Electronic and Communications Engineering
Dr Paul Curran
Room 145, Engineering.
paul.curran@ucd.ie
+353-1-7161846

## Slide 2: Overview of Topics
Mathematical background and problem statement.
Dominant pole placement via root locus.
Basic loop shaping.
Linear state feedback and observers.
Digital control.

## Slide 3
Section 2 - Outline
Feedback
Dominant Poles
Section: 2
System Response

## Slide 4: Note
In control theory we wish to partly change or add to a system so that its performance is improved. We must develop a measure of quality of performance, so that we are in a position to actually recognize improvement. Accordingly we must firstly give some consideration to how systems naturally tend to behave. There are two aspects of system behaviour, transient and steady-state. Roughly we are concerned with only two features of the transient: it should not last too long and it should not be such as to damage or destroy the system. The steady-state is much more significant. We commonly wish to specify exactly what it should be.
Section: 2
System Response

## Slide 5: Feedback
Control: Although a given system may achieve the required transformation from input signals of a certain physical form to output signals of a possibly distinct physical form, such a system will rarely behave as one would require.
e.g. An electric kettle will heat the water to boiling point and then proceeds to boil it away.
e.g. An electric fire converts electric energy to heat energy, but one may still feel cold.
Section: 2
System Response

## Slide 6
In the examples quoted above the problem of the behaviour of the system no doubt seems trivial. Just turn off the kettle when the water boils or turn up the fire if you feel cold.
However, these trivial solutions require the action of an agent external to the system. Something must observe that the kettle is boiling and stop the current or observe that you still feel cold and increase the current.
This external agent is called a Controller.
Section: 2
System Response

## Slide 7: Open Loop Control
The simplest control strategy is to allow an external agent take direct control of the input to the system: e.g. electric toaster
This is called open loop control. It is simple but commonly very poor.
Section: 2
System Response

## Slide 8: Note
Open loop control is poor because it cannot react to unforeseen problems. White goods such as washing machines commonly operate using open loop control. A red sock included with the white wash is a good illustration of unforeseen problems. An example of open loop control would be a strategy for leaving your house. You lock the door, get into the car, reverse out the gate, turn 90 degrees and accelerate up to 60 km per hour. This strategy works fine until one day the bin lorry is early. That is the problem with open loop control, it is a predefined strategy which is defined subject to assumptions. If the assumptions fail, for example the road is blocked, the strategy cannot be switched off. It must run (or try to run) its course, even when something has gone wrong.
Section: 2
System Response

## Slide 9
How does a human control a fire ?
Monitor output: feel heat of fire
Compare with desired output: feel hot or cold
Adjust input in manner which one knows will improve output: turn heat down (if hot) or up (if cold)
This is called closed loop control
Section: 2
System Response

## Slide 10: Note
Closed loop control monitors the output and adjusts the input accordingly. It takes the consequences of its actions into account. In the case of a red sock in the white wash closed loop control could, in principle, monitor the colour of the water and adjust its actions when the water starts to look pink.
The term closed loop gets its name for obvious reasons. The term open loop gets its name because the controller does not monitor the output and/or compare with a reference. In other words, in the above diagram the loop is broken at the point of monitoring and/or at the point of comparison.
Section: 2
System Response

## Slide 11: Note
A controller may be a human being. This is common in the form of pilots, drivers, etc.
Human controllers tend to be excellent except for their tendency to become tired or bored when the control task is repetitive or of significant duration. They then begin to reduce the quality of their monitoring or comparing of the system behaviour and effectively allow the system to revert to uncontrolled operation.
An automatic process for controlling a system is called an Automatic Controller. The body of knowledge for designing such processes is called Automatic Control.
This module is about automatic control. One of the technical devices which enables the implementation of certain control strategies (commonly open loop) is called a Programmable Logic Controller (PLC). This module is not about PLCs.
System Response
Section: 2

## Slide 12
How should we compare ?
It is commonly accepted that one should compare the actual output to the reference signal by subtracting.
The difference signal (Reference Signal - Monitored Output) is called the error signal.
This kind of loop is called a negative feedback loop.
Section: 2
System Response

## Slide 13: Classical examples of Automatic Control from modern perspective
Water clock (300 BC), flow of water held constant by negative feedback loop.
Watt flyball governor (1769), rotational velocity of shaft held constant by negative feedback loop.
Water-level float regulator, level held constant by negative feedback loop.
Section: 2
System Response
Notes: Need Dorf, page 5 and page 26. These negative feedback loops were intuitively defined.

## Slide 14: Negative Feedback
Section: 2
System Response
Although intuitively used by many cultures over the millennia, the official identification of the idea of negative feedback is rather recent, being due to Black. Black introduced the concept in order to improve the performance of electronic amplifiers. Prior to the incorporation of negative feedback amplifiers had very high gain but it was highly unstable, fluctuating significantly with temperature and with the specific device employed. Black argued that a process which would massively decrease the achieved gain, would massively improve stability and decrease sensitivity. It was at first a hard concept to sell.
Notes: Need Dorf, page 5 and page 26. These negative feedback loops were intuitively defined.

## Slide 15: Example 2.1
Section: 2
System Response
Consider again the robotic arm driven by a DC motor having the s-domain model (i.e. transfer function)
Consider incorporating this system within a standard negative feedback loop (actually we would call it a unity negative feedback loop to be precise).

## Slide 16
Example 2.1
Section: 2
System Response
e = r - qp is the error signal. The system with output e and input r is a linear time-invariant (LTI), single input/single output (SISO) system and therefore can be characterised by a transfer function.

## Slide 17
Example 2.1
Section: 2
System Response

## Slide 18: Note
With the block diagram models we find that the transfer function from input r to output e depends in part on the system, but critically depends also on the controller. If we have sufficient scope in designing the controller we may be able to achieve any desired closed-loop transfer function. Accordingly classical control theory reduces to two problems: (i) setting up target closed-loop transfer functions, i.e. identifying which transfer functions are desirable and (ii) designing controllers to achieve these desired closed-loop transfer functions.
Section: 2
System Response

## Slide 19: Specification and Reference
The control system is deemed to be working correctly provided the error signal goes to zero. In the present example, given the relatively simple control paradigm being used (namely unity negative feedback) should the error go to zero then it follows that the forced component of the angle of the arm will become equal to the reference signal. If it is desired that the arm should turn through a certain angle and if it is assumed that the arm is initially at rest, then we may take the initial angle to be zero, i.e. we just use this as our reference angle.
Section: 2
System Response

## Slide 20: Specification and Reference
To ensure that the final angle is some particular value j we should let the reference signal be:
Section: 2
System Response
For, if the error signal goes to zero, i.e. if the output tracks the reference signal, then the angle of the arm must become equal to the desired angle j. Here as usual u(t) denotes the unit step function. This factor reflects that prior to t = 0 we desired the arm to be at its initial angle and at t = 0 we change our mind and require that it move to the new desired angle.

## Slide 21: Specification and Reference
Section: 2
System Response
So our specification concerning the desired performance of the closed-loop system is that the output angle should track the special reference signal
In other words the error should go to zero. Of course this is an absolute minimal specification. In reality we will also require that the error goes to zero rather quickly. This type of problem is commonly referred to as a position control problem as we wish to set the long term (steady-state) position of the arm.

## Slide 22
Example 2.1
Section: 2
System Response
Problem 1 (position control)
Specification

## Slide 23
Example 2.1
Section: 2
System Response
Specification requires:

## Slide 24: Example 2.1
Within the block diagram model of the closed-loop system the input to the controller is the error signal e and the output is the motor voltage v. Suppose the controller is described within the time-domain by the following equation:
Section: 2
System Response
Using linearity and integration properties we have:

## Slide 25: Example 2.1
It follows that the transfer function of the controller is:
Section: 2
System Response
as required. The time-domain description:
reveals that the output is a sum of two components, one of which proportional to the input and one of which is proportional to the integral of the input. The controller is called a Proportional-Integral (PI) controller.

## Slide 26: Example 2.1
The electronic engineers among you will be aware that there are standard circuits involving operational amplifiers (op amps) which can be used to realise such a controller. Indeed one can buy off the shelf controllers essentially of this kind.
The as yet unknown parameters kp and ki are called the controller gains. The first is called the proportional gain and the second is called the integral gain. Just by virtue of having these terms the closed-loop system automatically solves the position control problem. The task of control is to pick values for these gains such that the error signal will not just go to zero (which is the absolute minimum requirement imposed in the unity negative feedback paradigm, but also so that other desirable things happen, eg the response is fast.
Section: 2
System Response

## Slide 27: Example 2.1
By selecting for the reference input a step we ensure that provided the closed-loop control system is functioning (i.e. provided the error goes to zero) then the output which is initially assumed to be zero will ultimately settle at the value of the reference input (or set point as some engineers call it). Having the output settle to a set point or desired value is not the only type of control problem which we may wish to solve. Sometimes we may desire the output velocity to settle to a desired value, as for example in the case of a train or some other vehicle. How might we achieve this?
Section: 2
System Response

## Slide 28: Example 2.1
The first step is to change the reference input. Instead of employing a step we may employ a ramp, i.e. set the reference input to
Section: 2
System Response
Now if the closed-loop control system is functioning then in the long run (i.e. the steady-state) the error signal will go to zero so that the output tracks the ramp. But the mathematical nature of the ramp is that it has a constant derivative v0. It follows that the steady-state derivative of the output will equal the set value v0, i.e. the output velocity becomes equal to this value. This is called velocity control.

## Slide 29
Example 2.1
Section: 2
System Response
Problem 2 (velocity control)
Specification

## Slide 30
Example 2.1
Section: 2
System Response
Specification requires:
This is a special case of a PI controller where the proportional terms is omitted. It is an I-controller or rather just an integrator.

## Slide 31: Feedback Control System
System Response
Section: 2
Generally assume ideal sensor: Gsens(s) = 1 and combine plant and controller to obtain
the open-loop transfer function

## Slide 32: Note
We begin to move towards more conventional control notation. G will from now on generally denote the transfer function of a system, suitably subscripted to identify the system (e.g. p for plant).
The system to be controlled is commonly called the plant or process. If the sensor is non-ideal it can simply be absorbed into the plant by defining the output of the closed-loop system to be the output of the sensor rather than the output of the plant. Since control system design is very commonly focussed on the error signal, it is not completely relevant which signal is deemed to be the output of the closed-loop system.
Section: 2
System Response

## Slide 33: Note
An ideal sensor will have a transfer function of unity since its output is simply equal to its input.
If the feedback loop is cut then the transfer function from r to y equals the open-loop transfer function. The open-loop transfer function describes the open-loop system.
Section: 2
System Response

## Slide 34: Feedback Control System
System Response
Section: 2
Open-loop transfer function
Closed-loop transfer function
Closed-loop characteristic polynomial

## Slide 35: Note
We assume all transfer functions to be rational polynomials (which we know they will be if, for example, the systems are described by linear, constant coefficient ODEs). The numerators are denoted N, the denominators are denoted D and both are subscripted by the system subscript (e.g. p for plant, c for controller).
The closed-loop characteristic polynomial is the denominator polynomial of the closed-loop transfer function, i.e. the transfer function from r to y. The roots of the closed-loop characteristic polynomial are the poles of the closed-loop transfer function and are called the closed-loop poles.
Section: 2
System Response

## Slide 36: Note
The discussion, in particular of example 7, in previous lectures suggests that the closed-loop poles will have a significant influence on the performance of the closed-loop system. The roots of the denominator polynomial D0(s) are the poles of the open-loop transfer function and are called the open-loop poles. Significantly the closed-loop poles and the open-loop poles do not have to be the same and indeed will generally not be the same.
The roots of the numerator polynomial N0(s) are called the open-loop zeros of the system. The roots of the numerator polynomial Ncl(s) are called the closed-loop zeros of the system. The formula indicates that the closed-loop zeros and the open-loop zeros are identical.
Section: 2
System Response

## Slide 37: Feedback Control System
System Response
Section: 2
A step is by far the most common reference input as it establishes a set point.

## Slide 38: Note
A reference equal to a step is more than common, it corresponds probably to the absolute majority. e.g. in temperature control the user suddenly turns the thermostat to a required temperature, essentially changing the required temperature (the reference) almost instantaneously between two settings.
By the homogeneity feature of linearity the response to any step is simply a suitable scaling of the response to a unit step. A significant portion of classical control is concerned with achieving an acceptable unit step response.
Section: 2
System Response

## Slide 39: Feedback Control System
System Response
Section: 2
We find the partial fraction expansion of Y(s). Of particular concern is the pole at s = 0. There is a clever procedure (sometimes called Heaviside’s method) for finding the associated coefficient in the partial fraction expansion. Employing this procedure we have:

## Slide 40: Feedback Control System
System Response
Section: 2
if Re(si) < 0 all i
Finally we may invert:

## Slide 41: Note
The output clearly converges to a constant value iff the closed-loop poles have negative real part (this also implies that the uncalculated free response converges to zero). In this event the output converges to the constant Gcl(0)r0. This is called the steady-state solution and we note that the ratio of this steady-state output to the steady-state input r0 equals Gcl(0).
Section: 2
System Response

## Slide 42: Feedback Control System
System Response
Section: 2
Rule 1: Minimum condition for acceptable step response:
The closed-loop system should be stable.
Definition*: A system is stable if all of its poles have negative real part.

## Slide 43: Note
Stability also ensures that the free response converges to zero thus justifying our ignoring it.
* The definition of stability given only holds under certain conditions. The system must be linear, time-invariant, finite-dimensional and have a transfer function which is a strictly proper rational polynomial. Minus any of these properties and the definition becomes meaningless. In fact the “definition” given is not actually a definition of stability, it is rather a test of stability.
Section: 2
System Response

## Slide 44: Feedback Control System
System Response
Section: 2
Rule 2: Minimum condition for acceptable step response:
The closed-loop DC gain should be unity.
Definition: The DC gain of a system equals the transfer function of the system evaluated at 0.
By above for step input r0u(t) and stable closed-loop system

## Slide 45: Note
The DC gain is so called because if the input to the system is a constant then, assuming the system to be stable, the steady-state output of the system will also be a constant being equal to the DC gain of the system times the input.
Rule 2 implies that the steady-state error e=r-y equals zero, i.e. the closed-loop is tracks the reference input.
Section: 2
System Response

## Slide 46: Feedback Control System
System Response
Section: 2
By above
Closed-loop DC gain equals unity implies
i.e. require pole at 0 or integrator in forward path
Usually achieved by

## Slide 47: Note
D0(0) = 0 implies that D0(s)=sD0’(s) for suitable polynomial D0’. It follows that G0(s) = (1/s)G0’(s) for suitable G0’. The transfer function of an ideal integrator is (1/s) hence the condition D0(0) = 0 implies that the open-loop system equals the cascade of an ideal integrator and a suitable subsystem. This is why we use the phrase “integrator in the forward path”.
Since the plant will not normally have a pole at zero (i.e. Dp(0) will normally be non-zero) this required integrator in the forward loop must be introduced by the controller. Indeed this is the purpose of the I-term in a PI controller.
Section: 2
System Response

## Slide 48: Feedback Control System
System Response
Section: 2
Rule 2: (Practical form) Minimum condition for acceptable step response (i.e. for perfect tracking):
The open-loop transfer function should have a pole at zero, usually achieved by the controller having a pole at zero.
PID Controller

## Slide 49: Feedback Control System
System Response
Section: 2
if Re(si) < 0 all i
So far we have set up a specification on the closed-loop system performance which ensures tracking of a step. Obviously this is insufficient, we require reasonably fast tracking. Recall:

## Slide 50: Dominant Poles
System Response
Section: 2
As Dcl(s) is a real polynomial the closed-loop poles occur in complex conjugate pairs. Two generic cases occur:

## Slide 51: First Order System
System Response
Section: 2
Consider the special system:
This is a first order system with time constant t and a DC gain of one. The system has one pole at s = -s.
The unit step response is:
which is similar to response of general system in Case 1.

## Slide 52: Note
Note that a short time constant implies a large negative pole. The time-constant is a good measure of the speed of response of the system. We may readily analyse the performance of first order systems. The point is not that they exist, they certainly do not, but rather that they offer good models for the behaviour of actual higher order systems which happen to have a dominant real pole.
Section: 2
System Response

## Slide 53: First Order System
System Response
Section: 2
Rule 3: In case 1 (dominant real pole) the system often behaves like a first order system. For improved speed of response require that the dominant pole lie as far to the left of the imaginary axis as possible.

## Slide 54: Note
The duration of the transient of a first order system is approximately 4 or 5 time constants (i.e. 0.4-0.5 sec in this case). We will generally assume a transient time of 5 time-constants in this module. It is important to appreciate that a higher order system having a dominant real pole will only behave like a first order system once the dominated terms in the actual system response have decayed away, and this takes time. Many authors appear to forget this fact, employing approximate first order models, observing “early phase” properties of those models and suggesting that the higher order system will approximately have these properties. They may do, but it will be down to luck not logic.
Section: 2
System Response

## Slide 55
>> step([1],[0.1 1])
Section: 2
Code
System Response

## Slide 56: Dominant Real Pole: Specification
System Response
Section: 2
It is very common to characterise required system behaviour through specification of the step response. In the case of a system with a dominant real pole this response may be similar to the step response of a first order system.
Specification: DC gain = 1, transient time
Dominant real pole to left of Re(s) = -5 implies all closed-loop poles to left of Re(s) = -5.

## Slide 57: Note
A first order response is specified by two characteristics: speed of response and steady-state.
The specs have been transformed into a simple statement about the forward path (it must contain a pole at 0) and a statement about the required location in the complex plane of the closed-loop poles (they must lie to the left of a line parallel to the imaginary axis). The only additional constraint is that the closed-loop system must actually have a dominant real pole.
This specification embraces the requirements of stability.
Section: 2
System Response

## Slide 58: Note
We could describe the outlined methodology as a model reference approach. We identify a simple model (a first order transfer function). We determine the parameters of this model such that were the closed-loop system actually described by this simple model it would meet all of the specifications (where we have made essentially all of those specifications with a view to achieving a desirable step response). Now the controller must be designed so that the closed-loop system actually behaves approximately like the simple model and therefore meets the specification because the simple model meets the specification.
Section: 2
System Response

## Slide 59: Second Order System
System Response
Section: 2
Consider the special system:
This is a second order system with natural frequency wn, damping ratio z and a DC gain of one. The system has a complex conjugate pair of poles.
Unit step response:
which is similar to response of general system in Case 2.

## Slide 60: Note
Again we may readily analyse the performance of second order systems. As before the point is not that they exist, they certainly do not, but rather that they offer good models for the behaviour of actual higher order systems which happen to have a dominant pair of poles.
Section: 2
System Response

## Slide 61: Second Order System
System Response
Section: 2
We observe two new phenomena: overshoot and ringing.
Overshoot: The output shoots past its steady-state value.
Ringing: The output oscillates about steady-state value.

## Slide 62
>> step([1],[1 0.4 1])
Section: 2
Code
System Response

## Slide 63: Second Order System
System Response
Section: 2
Definition: The 2% settling-time, ts(2%), is the time it takes for the output to settle inside the 2% band around the steady-state value.
Analysis of the second order system yields:

## Slide 64: Second Order System
System Response
Section: 2
Definition: The Percentage Overshoot, PO, is the size of the overshoot expressed as a percentage of the steady-state value.
Analysis of the second order system yields:

## Slide 65: Note
A point to note is that the percentage overshoot depends upon the damping ratio but not upon the natural frequency. This kind of thing is always useful in design since it permits a divide-and-conquer approach to the design task.
Section: 2
System Response

## Slide 66: Second Order System
System Response
Section: 2
Recall that the poles are
Hence
The poles lie on the boundary of a sector about the negative real axis. PO depends on sector angle f only.

## Slide 67: Note
The left half-plane sector bounded by the poles uniquely determines PO and vice versa. For increased z, the imaginary part reduces relative to the magnitude of the real part, the sector narrows and of course the PO decreases. Hence for small PO one requires a narrow sector.
Section: 2
System Response

## Slide 68: Second Order System
System Response
Section: 2
Rule 4: In case 2 (dominant pair) the system often behaves like a second order system. For improved speed of response require that pair lie far to the left of the imaginary axis. For reduced overshoot require that pair lie inside a sufficiently narrow sector about the negative real axis.

## Slide 69: Dominant Pair: Specification
System Response
Section: 2
Characterise through specification of the step response. In the case of a system with a dominant pair this response may be similar to the step response of a second order system.
Dominant pair to left of Re(s) = -2 and inside sector of angle f. In practice require that all poles lie in this region.
Specification: DC gain = 1,

## Slide 70: Note
Again specification transformed to simple expression concerning the forward path (it must contain a pole at 0) and a statement about the required location in the complex plane of the closed-loop poles (they must lie to the left of a line parallel to the imaginary axis and inside a sector about the negative real axis). The only additional constraint is that the closed-loop system must actually have a dominant pair. Of course this specification embraces the requirements of stability.
Section: 2
System Response

## Slide 71: Note
Again we a model reference approach. We identify a simple model (a second order transfer function). We determine the parameters of this model such that were the closed-loop system actually described by this simple model it would meet all of the specifications (where we have made essentially all of those specifications with a view to achieving a desirable step response). Again the controller must be designed so that the closed-loop system actually behaves approximately like the simple model and therefore meets the specification because the simple model meets the specification.
Section: 2
System Response

## Slide 72: Dominant Pole Placement
System Response
Section: 2
Textbooks commonly devote a great deal of space to the analysis of first and second order systems. The reason for this attention is not that such systems arise so often, but rather that very many engineering systems, when operating close to a desired operating point stable, can be linearised and the resulting LTI, SISO system will have either a dominant real pole or a dominant pair and will therefore be tolerably well approximated by a suitably chosen first or second order system. Accordingly the time expended in the analysis of first and second order systems is amply rewarded by the applicability of the results to a very wide, almost ubiquitous, class of systems.

## Slide 73: Dominant Pole Placement
System Response
Section: 2
Within this context it is in the nature of negative feedback to reinforce the validity of this long list of assumptions. The controller keeps the system close to the operating point so that the linearisation (a.k.a the small signal analysis remains valid), the negative feedback also reduces the sensitivity of the closed-loop system performance to the open-loop performance. Accordingly taking rather poor models for the open-loop system, i.e. for the plant, is more readily justified.

## Slide 74
First Order System
Section: 2
System Response
Specification: | Symbol: | Approximation:
10% to 90% rise time | tr | 
Settling time | ts(2%) ts(5%) | 
Overshoot | PO% | 0%

## Slide 75: Note
System Response
Section: 2
This table is typical of the information sought and acquired through an analysis of a first order system.
The 10% to 90% rise time (also known as simply the rise time) is another method of estimating the transient time. It is equal to the time which must elapse between the step response first reaching 10% of its steady state value to first reaching 90% of its steady state value.
I do not regard it as reliable in its capacity to estimate the transient time. My reason is that it is based upon the initial or early phase response of the first order system, where in practice it is least like the actual response of the high order system.

## Slide 76: Note
System Response
Section: 2
However the rise time is very important for an entirely different reason. It offers a test for whether the actual control system can be expected to behave according to the theory. If the supposed rise time of the closed-loop system is ridiculously small in comparison with the natural rise time of the plant then one must suspect that the solution offered is purely academic. It is rather easy to offer solutions of this kind since they are divorced from the physical realities of the world. In effect we make a host of assumptions which simply do not hold.

## Slide 77
Formulae approximate even for second order systems
because they assume a special form for the numerator.
Accordingly we employ them with a very strong caveat.
Section: 2
Second Order System
System Response

## Slide 78: Note
Formulae for time to overshoot and overshoot are exact for canonical second order system. The formulae for the settling times are reasonable approximations for the second order canonical system. The formula for rise time is hard to acquire.
Section: 2
System Response

## Slide 79
Section 2 - Conclusion
Negative feedback affects a commonly positive change in the behaviour of a control system.
The unit step response of a closed-loop system is an important measure of system performance and is largely determined by the location of the closed-loop poles, particularly if certain poles are dominant.
Speed of response usually improves if poles are pushed further into the left half plane.
Overshoot is usually reduced if poles are restricted to a narrower sector about negative real axis.
Perfect tracking requires the presence of an integrator in the forward path.
Section: 2
System Response