## Slide 1
Control Systems
Stage 4: Electrical, Electronic and Communications Engineering
Dr Paul Curran
Room 145, Engineering.
paul.curran@ucd.ie
+353-1-7161846

## Slide 2: Overview of Topics
Mathematical background and problem statement.
Dominant pole placement via root locus.
Basic loop shaping.
Linear state feedback and observers.
Digital control.

## Slide 3
Section 4 - Outline
Frequency response
Bode plots and system identification
Nyquist stability criterion
Stability margins, gain and phase crossover frequencies and performance, system type
Section: 4
Frequency Response

## Slide 4
Section: 4
Frequency Response
Sinusoidal Steady State Response
Referring to the end of the mathematical background notes I have that if a linear, constant-coefficient ODE has forcing term cos(wt) then the forced response (i.e. the particular solution satisfying zero initial conditions) is Acos(wt+f) where
where G(s) is the transfer function of the associated linear, time-invariant system. This result holds in fact for almost arbitrary LTI systems, not just those described by linear, constant-coefficient ODEs. Moreover, this result does not hold at all, there is are assumptions being made.

## Slide 5
Section: 4
Frequency Response
Sinusoidal Steady State Response
Let us engage by means of the Laplace transform. Since I can I will also generalise the result.
Hence if the transfer function is a rational polynomial G(s) then the forced response in the s-domain is

## Slide 6
Section: 4
Frequency Response
Sinusoidal Steady State Response
where the si are the poles of G(s), i.e. the roots of D(s) assuming none of these equal jw0.

## Slide 7
Section: 4
Frequency Response
Sinusoidal Steady State Response
I will assume that the system is stable, i.e. that the poles lie in the LHP. It follows that each of the si has negative real part. Of course this implies that none of them equal jw0 as required. I deduce that in the steady-state
Likewise:

## Slide 8
Section: 4
Frequency Response
Sinusoidal Steady State Response
Now Heaviside offers a simple method for determining the coefficients of the partial fraction expansion. Employing this method we obtain:
Hence the steady-state response to input A0cos(w0t+f0) equals:
The last critical observation is that since G(s) is a real rational polynomial

## Slide 9
Section: 4
Frequency Response
Sinusoidal Steady State Response
So the steady-state response to input A0cos(w0t+f0) equals:
i.e. a co-sinusoid of the same frequency but with amplitude and phase modulated by the modulus and argument of the transfer function evaluated at s = jw0.

## Slide 10: Note
This fundamental result from linear systems theory is the basis for the frequency-domain methods in control theory. The steady-state response of the system to sinusoidal inputs is called the frequency response of the system. The result above establishes that the frequency response is summarized by the complex function G(jw) where G(s) is the transfer function. In practice, since we cannot determine this complex function, we are content to calculate the complex numbers G(jwi) at the particular frequencies wi. If these frequencies are sufficiently numerous and well distributed they can give a fairly good sense of the complex function of which they are samples.
Section: 4
Frequency Response

## Slide 11
Section: 4
Frequency Response
The frequency response method has certain practical advantages when modelling transfer functions from physical data. The physical data referred to is “frequency response data” obtained by applying sinusoids of various frequencies as input to the system and measuring the amplitude and phase (or to be precise phase shift) of the resulting steady-state output. The result above asserts that the ratio of the output to the input amplitudes equals the magnitude of the transfer function and that the phase shift equals the argument (or phase) of the transfer function at the frequency in question. Accordingly, the frequency response of a system is amenable to experimental determination.
Notes: Of course theorem 4 only asserts this if the system really is LTI, SISO, causal, stable.

## Slide 12
Section: 4
Frequency Response
A second advantage of the frequency response method is that, whereas the time-domain methods considered above (i.e. pole placement) essentially assume all transfer functions arising in the course of the design are rational polynomials, the frequency response methods make no such assumption. Accordingly these methods can be applied to a system incorporating transport delay.
Transfer function of pure delay:

## Slide 13: Note
L denotes “latency” an alternative name for delay.
In reality delay is an ubiquitous feature of practical systems, so methods which cannot cope with delay must be viewed with some scepticism.
Section: 4
Frequency Response

## Slide 14: Example 4: reprieve
The simple suspension system of example 4 in the mathematical background material is an example, par excellence, of the frequency response and its utility.
Section: 4
Frequency Response
Assume k = 1, m = 1, m = 0.1 then

## Slide 15: Example 4: reprieve
Section: 4
Frequency Response
>> w = [0:0.01:5]; create vector of uniformly spaced frequencies over range of interest
>> Np = [1], Dp = [1 0.1 1]
>> Gpsamp = polyval(Np,i*w)./polyval(Dp,i*w);
>> plot(w,abs(Gpsamp))
>> xlabel('\omega (rad/sec) ')
>> ylabel('|G(j \omega)|')

## Slide 16
Section: 4
Frequency Response
Resonance
The plot of the magnitude (modulus) of G(jw) vs w is called the magnitude plot. We interpret it as telling us which frequencies are amplified by the system and which are attenuated.
As previously noted the magnitude response indicates the presence of resonant frequencies.

## Slide 17: Note
A low damping ratio will in general result in a significant peak in the frequency response. Such a peak, as noted previously, corresponds to resonance, i.e. the potentially significant amplification of an input signal amplitude. In practice any plant is subjected to disturbances (e.g. a car is subjected to buffeting by the wind). These disturbances are usually noisy (i.e. random to some extent). They are not sinusoids but, nevertheless they effectively have Fourier transforms (i.e. spectra) and these spectra may contain some spikes, i.e. some frequency components which are particularly strong. If a disturbance spectrum contains a spike close to a resonant frequency of the system, then this frequency component may be amplified, possibly to the detriment of the system.
Section: 4
Frequency Response

## Slide 18: Note
Section: 4
Frequency Response
As a general rule therefore it would be better for a closed-loop system to possess no resonances, as these are built in weaknesses. But to declare that the system is to have no resonance is to make a declaration concerning the frequency response of the system. We find that we cannot live with specifications concerning step response alone when specifying closed-loop system performance. We sometimes need to specify features of the frequency response.
The frequency response of a system can be viewed in two different ways: the Bode plot and the Nyquist diagram. Both methods display the same information; the difference lies in the way the information is presented. We will study both methods.

## Slide 19
Example 4.1:
Section: 4
Frequency Response
Bode Magnitude Plot
Bode Phase Plot

## Slide 20: Code
Section: 4
Frequency Response
>> Np = [50], Dp = [1 9 30 40]
>> Gp = tf(Np,Dp)
>> bode(Gp)
The Bode plots are plots of the magnitude (in dB) and phase (in degrees) of the transfer function versus the frequency (in rad/sec) with the latter plotted on a logarithmic scale. Note that unity gain in magnitude is equal to a gain of zero dB.
This does not explain why Bode chose to represent the frequency response data in this particular (and hardly obvious) way. In general a slightly strange solution to a problem usually indicates that the original author(s) were not thinking about that problem.

## Slide 21: Note
The problem which exercised Bode was not the graphical representation of frequency response data. It was the problem of finding the transfer function of the system from the frequency response data (which as noted above could be found experimentally), i.e. it was the problem of system identification. To illustrate his main idea let us take an example and commence with a rearrangement of the transfer function.
Section: 4
Frequency Response

## Slide 22
System Identification
Section: 4
Frequency Response

## Slide 23: Note
One immediate consequence of Bode’s decision to plot the magnitude in dB (i.e. logarithmically) is that the multiplicative interaction of the components of the transfer function is transformed into an additive interaction or superposition of the associated logarithmic components.
Section: 4
Frequency Response

## Slide 24
System Identification
Section: 4
Frequency Response

## Slide 25
Low Frequency Asymptote
Section: 4
Frequency Response
The low frequency asymptote is a line with a slope of -20q dB per decade. The slope of this line therefore tells us q, the order of the pole at zero.
Value of phase at low frequency also tells us q.

## Slide 26: Note
This is because the remaining terms all become approximately equal to 20log10(1) and this, of course, is zero. It is for this reason that the vital rearrangement of the transfer function was made above.
The next point to observe is that since Bode is concerned with physical systems he can be assured that the impulse response is a real function, i.e. that the system is real. Accordingly G(jw)=G(-jw)* (i.e. the complex conjugate) for all w. It follows that one may entirely ignore negative frequency, since information concerning the response of the system to such frequencies is entirely subsumed by information concerning the response to non-negative frequencies and it is the latter which we are able to determine experimentally. Indeed it is this symmetry (Hermitian symmetry to be precise) which explains why as human beings we are unaware of negative frequency. Negative frequencies always appear as one of a matching pair, with their twins being positive frequencies.
Section: 4
Frequency Response

## Slide 27: Note
Moreover, if Bode ensures that his transfer function is a real mathematical function then by fitting the frequency response of the mathematical function to the experimental frequency response over the non-negative frequency range he automatically fits the response over the entire frequency range. This is a very longwinded way of observing that the Bode plots can be, and therefore are, defined over the non-negative frequency range only.
Now because the horizontal axis of the Bode magnitude plot is log10(w) the above approximation describes a line with slope -20q. Because of the units on the axes of the Bode magnitude plot the units of this slope will be dB per decade because the magnitude will fall by 20q dB for every decade increase in frequency, where a decade increase means a multiplication by 10.
Section: 4
Frequency Response

## Slide 28: Note
The important point is that by examining the magnitude plot we can actually see that it is approximately equal to a line at low frequencies and we can determine the slope (in dB/decade) of this line. The information in this case that this slope is -20q dB/decade informs us from the frequency response that the transfer function must have a pole of order q at the origin. In short if I assume the system can be modelled by a rational polynomial transfer function, then I can begin to acquire some information concerning which particular rational polynomial offers the best model, or at least a good model.
Section: 4
Frequency Response

## Slide 29
Section: 5
Frequency Response
Low frequency asymptote: zero slope. Low frequency phase: zero degrees.
Conclude that the system has no pole at the origin. Yes I already knew this in the present case, but the point is that I can see it from the Bode plots.
Example 4.1:

## Slide 30
High Frequency Asymptote
Section: 4
Frequency Response
The high frequency asymptote is a line with a slope of -20(n-m) dB per decade. The slope of this line therefore tells us n-m, the relative degree.

## Slide 31: Note
n is the degree of the denominator polynomial (q +2 in this case) and m is the degree of the numerator polynomial. Again the decision to plot frequency on a logarithmic (base 10) scale ensures that the above expression describes a line (just as in the case of the low frequency approximation). This line, which approximates the high frequency response is called the high-frequency asymptote. The slope of this line is -20(n-m) dB/decade. It follows that this asymptote, in the form of its slope, contains very important information concerning the transfer function, namely the relative degree, n-m.
Section: 4
Frequency Response

## Slide 32
High Frequency Asymptote
Section: 4
Frequency Response
Value of high frequency phase also tells us n-m, the relative degree.

## Slide 33
Example 4.1
Section: 4
Frequency Response
High frequency asymptote: slope = -60 dB/dec.
High frequency phase: - 270 degrees.
Conclude that the system has relative degree of 3. Again I already knew this but the point is that I can see it from the Bode plots.

## Slide 34: Note
The order of the system (i.e. the degree of D(s)) is very significant. The relative degree does not tell us the order, but it certainly gives us useful information in this direction.
Bode went on to show how a great deal more information concerning the rearranged transfer function could be extracted from his plots of the frequency response data. It is fair to say that much of this detailed analysis has been overtaken by the advance in numerical tools. But some remains useful for design.
Section: 4
Frequency Response

## Slide 35
Approximations
Section: 4
Frequency Response
Consider term (s+1) :
Note good accuracy of piecewise linear approximation.

## Slide 36
Approximations
Section: 4
Frequency Response
Consider term 1/(0.5s+1) :
Note good accuracy of piecewise linear approximation.

## Slide 37
Approximations
Section: 4
Frequency Response
Consider term 1/(0.1s+1) :
General result for term (ts+1)±1 should now be clear.

## Slide 38
Approximations
Section: 4
Frequency Response
Consider term 1/s :

## Slide 39
Approximations
Section: 4
Frequency Response
Individual approximations.
Sum of approximations (blue) and actual magnitude plot (red).

## Slide 40: Note
In a similar manner the approximations for the individual components of the phase may be added to give an approximation to the phase plot.
Section: 4
Frequency Response

## Slide 41
Nyquist Criterion
Section: 4
Frequency Response
The zeros of F(s) are the closed-loop poles.
The poles of F(s) are the open-loop poles.

## Slide 42
Cauchy’s Principle of the Argument
Section: 4
Frequency Response

## Slide 43
Cauchy’s Principle of the Argument
Section: 4
Frequency Response

## Slide 44: Note
So, no net change if pole/zero is outside curve. Decrease by 2p if pole/zero is inside curve.
Argument of F(s) decreases by (Z-P)2p, where Z = number of zeros of F inside curve, P = number of poles of F inside curve, number being counted with multiplicity.
Section: 4
Frequency Response

## Slide 45
Cauchy’s Principle of the Argument
Section: 5
Frequency Response

## Slide 46: Note
Section: 4
Frequency Response
Although the example makes the principle seem plausible for all rational polynomials F(s), the principle actually holds for a much larger class of functions.
The principle of the argument can give us important information about the location of the poles and zeros of general functions.

## Slide 47
Nyquist Contour
Section: 4
Frequency Response
We employ the principle of the argument with a special choice of curve: the Nyquist contour.
If no open-loop poles are in RHP, then P = 0.
Stability requires that
Z = 0
i.e. that no zeros of F(s) lie inside Nyquist contour.

## Slide 48: Nyquist Stability Criterion
Section: 4
Frequency Response
Plot Go(s) for each s on the Nyquist contour, Gc.
This plot is called the Nyquist plot of Go(s).
Being the image of a closed curve, the Nyquist plot is also a closed curve.
Z, the number of zeros of F(s) inside Gc is equal to (decrease in Arg(F(s)))/2p.

## Slide 49: Nyquist Stability Criterion
Section: 4
Frequency Response
Z, the number of zeros of F(s) inside Gc is equal to (decrease in Arg(F(s)))/2p.
This equals the net number of clockwise encirclements of the origin by the image of Gc under the mapping F(s).
As F(s) = 1+Go(s) the image of Gc under F(s) is equal to the image of Gc under Go(s) shifted to the right by one unit.
Hence Z equals the net number of clockwise encirclements of the point -1 by the image of Gc under the mapping Go(s). Of course this image is the Nyquist plot.

## Slide 50: Note
Note that the shift by one unit to the right brings the point -1 to the origin.
For stability, assuming no open-loop poles in RHP, the net number of clockwise encirclements of the point -1 by the Nyquist plot should be zero.
Section: 4
Frequency Response

## Slide 51: Example 4.2
Section: 4
Frequency Response

## Slide 52: Code
Section: 4
Frequency Response
>> Np = [1], Dp = [0.1 1]
>> Go = tf(Np,Dp)
>> nyquist(Go)
The image of the semi-circular arc at infinity is zero. The image of the positive imaginary axis involves Go(jw) for w non-negative. The image of the negative imaginary axis is the conjugate, i.e. the reflection of the former image through the real axis.
Open-loop poles are -10 only in LHP. Clearly no CW encirclements of -1, hence stable. Evidently true as zeros of F(s) are -20 only.

## Slide 53
A difficulty arises if open-loop transfer function Go(s) has poles on the Nyquist contour. This most commonly arises when Go(s) has a pole at 0, required for perfect tracking. The principle of the argument does not apply in this case.
The resolution is to amend the Nyquist contour.
Section: 4
Frequency Response

## Slide 54: Example 4.3
Section: 4
Frequency Response
Image of semicircular arc at 0
= semicircular CW arc at infinity.

## Slide 55: Code
Section: 4
Frequency Response
>> Np = [1], Dp = [0.1 1 0]
>> Go = tf(Np,Dp)
>> nyquist(Go)
The image of the semi-circular arc at infinity is zero. The image of the semi-circular arc at 0 is (1/e)exp(-jq); q varying from –p/2 through 0 to +p/2. The image of the positive imaginary axis involves Go(jw) for w positive. The image of the negative real axis is the conjugate, i.e. the reflection in the real axis. Note that Matlab does not show the semi-circular arc at infinity.
Open-loop poles are -10 only in LHP. Clearly no CW encirclements of -1, hence stable. Evidently true as zeros of F(s) are -20 only.

## Slide 56
A variation occurs if the open-loop transfer function has the form kG'o(s), with explicit design parameter k.
Assuming the open-loop system is stable it follows that the closed-loop system is stable if and only if the net number of clockwise encirclements of the point (-1/k) by the Nyquist plot of G'o(s) is zero.
Section: 4
Frequency Response

## Slide 57: Example 4.4
Section: 4
Frequency Response
Stable if
Unstable if

## Slide 58: Code
Section: 4
Frequency Response
>> No = [1], Do = [1 2 1 0]
>> Go = tf(No,Do)
>> nyquist(Go)
Outer loop, not shown, encompasses RHP.
Dcl(s) = s3+2s2+s+k, so stability result is not obvious in this case. In fact in the unstable case where k>2 there are two closed-loop poles in RHP.

## Slide 59: Example 4.4
Section: 4
Frequency Response
Root locus confirms stability if k small (i.e. < 2).
Root locus confirms two poles in RHP if k large (i.e. > 2).

## Slide 60: Note
Root locus and Nyquist plot provide some common information. Can employ Routh-Hurwitz criterion to determine that k = 2 is the transition value, but much easier to employ rlocfind.
Section: 4
Frequency Response

## Slide 61
Gain Margins
In example 4.4 the closed-loop system is stable for 0 < k < 2. If k = 1 is considered “nominal” then the gain parameter k can be doubled before stability is compromised.
Section: 4
Frequency Response
The upper gain margin is a measure of the increase in open-loop gain required to render the system unstable.
Systems with greater upper gain margins can withstand greater increases in system gain parameters before becoming unstable in closed loop.

## Slide 62: Note
Here, kupper is the first value of k above nominal for which the system is marginally stable.
Section: 4
Frequency Response

## Slide 63
Gain Margins
In example 4.4 with k = 1 considered “nominal”, the gain parameter k can be arbitrarily (multiplicatively) reduced before stability is compromised.
Section: 4
Frequency Response
The lower gain margin is a measure of the decrease in open-loop gain required to render the system unstable.
Systems with greater lower gain margins can withstand greater decreases in system gain parameters before becoming unstable in closed loop.

## Slide 64: Note
Here, klower is the first value of k below nominal for which the system is marginally stable.
In case it is unclear we are restricting our attention to positive gains only.
Section: 4
Frequency Response

## Slide 65
Gain Margins
Gain margins can be read off the Bode plots, assuming knominal = 1. A frequency for which
Section: 4
Frequency Response
is called a phase crossover frequency.
For example 4.4 the Bode plot is shown. The phase crossover frequency is approx. 1 rad/sec.
The gain at this frequency is approx. -6 dB which is minus the upper gain margin.

## Slide 66: Note
To see this note that with F(s) = 1+kGo(s) stability implies that the zeros of this function have negative real part and instability that at least one of them has positive real part. Accordingly at the edge of stability at least one of the zeros of this function has zero real part, i.e. is on the imaginary axis. Hence F(s) = 0 holds for some s = jw. Equivalently:
The argument constraint asserts that w is a phase crossover frequency and the modulus constraint that k in dB is minus the gain in dB at this frequency.
Frequency Response
Section: 4

## Slide 67: Note
It is called the phase crossover frequency if there is only one, which is not uncommon.
The gain at phase crossover is minus the upper gain margin if it is the first phase crossover frequency with a gain below 0 dB. The gain at phase crossover is the lower gain margin if it is the first phase crossover frequency with a gain exceeding 0 dB. If there is no such frequency then the lower gain margin is infinity dB.
Section: 4
Frequency Response

## Slide 68
Phase Margin
The gain margin measures by how much a gain term k in an open-loop transfer function kGo(s) can vary from a nominal value of k = 1 before stability is compromised.
Likewise the phase margin is a measure of how much a phase f in an open-loop transfer function exp(-jf)Go(s) can vary from nominal value of f = 0 before stability is compromised.
Section: 4
Frequency Response

## Slide 69
Phase Margin
Phase margin can be read off the Bode plots, assuming knominal = 1. A frequency for which
Section: 4
Frequency Response
is called a gain crossover frequency.
For example 4.4 the Bode plot is shown. The gain crossover frequency is approx. 0.7 rad/sec.
The phase at this frequency is approx. -160o so phase margin is 20o.

## Slide 70: Note
It is called the gain crossover frequency if there is only one, which is very uncommon.
The phase margin is 180o plus the phase at gain crossover.
A change in phase term rotates the Nyquist plot. A rotation by PM implies that a critical stability point occurs at the gain crossover frequency.
Section: 4
Frequency Response

## Slide 71: Note
Note again that with F(s) = 1+e-jfGo(s) stability implies that the zeros of this function have negative real part and instability that at least one of them has positive real part. Accordingly at the edge of stability at least one of the zeros of this function has zero real part, i.e. is on the imaginary axis. Hence F(s) = 0 holds for some s = jw. Equivalently:
The modulus constraint asserts that w is a gain crossover frequency and the argument constraint that f in degrees is 180o plus the phase at this frequency.

## Slide 72
Delay Margin
Section: 4
Frequency Response
I find most of the standard justifications for the importance of the phase margin to be rather contrived. In my opinion the phase margin is not terribly important in its own right. However it is strongly related to two quantities which are vitally important. We have not considered modelling delay yet, although the reality is that it is present. Of concern then is how much previously un-modelled delay can be introduced to a system before stability is compromised. If it is terribly small then we are in trouble because the actual un-modelled delay will probably exceed it.

## Slide 73
Delay Margin
Section: 4
Frequency Response
A pure time delay can be modelled as a block with
transfer function:
Such a block adds phase to (or more precisely subtracts
phase from) the system but has no effect on the gain since:
Block manipulation reveals that the closed-loop poles of the delay-free system with previously un-modelled delay now delay are the roots of the equation:

## Slide 74
Delay Margin
Section: 4
Frequency Response
Alternatively:
The roots of this equation are the closed-loop poles, but this
is far more complicated than a polynomial equation. For
example consider the very simple case:

## Slide 75
Delay Margin
Section: 4
Frequency Response
The key difference between this and the delay-free case is
that in the presence of any non-zero delay this equation has
infinitely many solutions, essentially one for each choice of integer k. In short, even a first order system with delay
behaves like a system of infinite order, in the sense that its
root locus has infinitely many branches. Clearly this implies that the root locus procedure is not well suited to deal with these systems. The Bode plots on the other hand have no problem at all.

## Slide 76
Delay Margin
Section: 4
Frequency Response
Assuming a nominal time delay of zero the delay margin
is a measure of the maximum delay that can be introduced
before stability is compromised.
Note that at the edge of stability the closed-loop poles
must lie in the closed LHP with at least one on the
imaginary axis, i.e. at the edge of stability
has a non-negative solution w, i.e.

## Slide 77
Delay Margin
Section: 4
Frequency Response
Assuming there is only one gain crossover frequency:

## Slide 78: Note
We get here not only a simple formula for the delay margin but also a justification for the significance of the phase margin, which was defined, but not justified above. The importance of DM is clear, since systems will have un-modelled transport delay. The importance of PM is unclear since a multiplicative phase term exp(-jf) seems hard to argue when the transfer functions are real. But large PM is now seen to imply large DM. The PM is important because the DM is important. The formula is our only way of finding the DM, it cannot be read directly off the Bode plots. The PM can be so obtained and this is one reason why we pay it such heed.
Section: 4
Frequency Response

## Slide 79
Stability Margins
Section: 4
Frequency Response
For example 4.4: using margin command

## Slide 80: Code
Section: 4
Frequency Response
>> No = [1], Do = [1 2 1 0]
>> Go = tf(No,Do)
>> margin(Go)
Note agreement with previous results.

## Slide 81: Note
Why do I call the Gain Margin (i.e. Upper Gain Margin) and Phase Margin stability margins ?
Well the answer is that these margins, whereas they can be read from the Bode plot, also tell me something about the Nyquist plot. In fact, subject to a number of assumptions, I find that it is commonly the case that if the GM and the PM of the open-loop system are positive, then the closed-loop system can be shown to be stable by the Nqyuist criterion. On the other hand if either the GM or the PM or both are negative then the closed-loop system can commonly be shown to be unstable by applying the Nyquist criterion.
The relationship between the sign of the stability margins and stability of the closed-loop systems is subtle, but roughly speaking positive margins imply stability and negative margins instability.
Section: 4
Frequency Response

## Slide 82
Stability Margins and Stability
Section: 4
Frequency Response
Example :

## Slide 83: Note
Where the phase is -180o, i.e. at the phase crossover frequency (3.1623 rad/sec), the gain is -5.571 dB, i.e. it is less than 0 dB.
On the Nyquist plot this means that where the plot cuts through the negative real axis it does so at a point of magnitude less than 1, i.e. the Nyquist plot does not encircle the point -1+j0 since this point is to the left of the plot.
Where the gain is 0 dB, i.e. at the gain crossover frequency (2.4211 rad/sec), the phase is -150o approx, i.e. it is more than -180o.
On the Nyquist plot this means that where the plot cuts into the unit circle it does so at a point of lying below the real axis, i.e. again the Nyquist plot does not encircle the point -1+j0 since again this point is to the left of the plot.
Section: 4
Frequency Response

## Slide 84
Stability Margins and Stability
Section: 4
Frequency Response
Example :

## Slide 85: Note
Where the phase is -180o, i.e. at the phase crossover frequency (rad/sec), the gain is about 13 dB, i.e. it is more than 0 dB.
On the Nyquist plot this means that where the plot cuts through the negative real axis it does so at a point of magnitude more than 1, i.e. the Nyquist plot encircles the point -1+j0.
Where the gain is 0 dB, i.e. at the gain crossover frequency (rad/sec), the phase is -210o approx, i.e. it is less than -180o.
On the Nyquist plot this means that where the plot cuts into the unit circle it does so at a point of lying above the real axis, i.e. again the Nyquist plot encircles the point -1+j0.
Section: 4
Frequency Response

## Slide 86
Just as system performance (or at least step response) can be characterised in terms of dominant pole locations (time-domain spec.), so also it can be specified in terms of frequency domain characteristics. If it exists the gain crossover frequency (or the largest such frequency in the case where there is more than one) is the highest frequency at which the open loop gain is 1. For all higher frequencies the gain will fall away towards 0. The gain crossover frequency is therefore some kind of measure of the highest frequency to which the system can react.
Actually this statement is far more correct if I specify that I am speaking of the closed-loop gain crossover frequency, not the open-loop gain crossover frequency, although it is the latter which I am more likely to know.
Frequency Response
Section: 4
Bandwidth

## Slide 87
If a system can react to very high frequencies then it must be rather fast. So a high gain crossover frequency may be expected to correspond to a quick response, i.e. short settling time.
Of course if the gain crossover frequency is low then the system cannot react to high frequencies and must be expected to be slow, i.e. to have a long settling time.
Unfortunately many systems do not have a gain crossover frequency. This occurs if the gain is below 1 (i.e. 0 dB) across the entire frequency range.
Frequency Response
Section: 4
Bandwidth

## Slide 88
The bandwidth is the frequency range from DC up to a frequency having the property that for all frequencies beyond this critical frequency the system gain is 3 dB below the DC gain.
We will denote the upper edge of this frequency range by .
The bandwidth then is also a measure of the highest frequency to which the system can react and again we expect that high bandwidth means fast response and low bandwidth means slow response.
Frequency Response
Section: 4
Bandwidth

## Slide 89
The advantage of the bandwidth is that it is defined for all systems having a high frequency roll off, i.e. for all practical systems. As noted before, the gain crossover frequency is not always defined, most notably if the DC gain is less than 0 dB.
If a system has DC gain less than 0 dB it also has a steady state error to a step which is high (as we will see more clearly later). We would generally include a proportional gain in series with the system to increase the DC gain and thereby reduce this error. If the DC gain is raised to 3 dB then the gain crossover frequency of the new system is equal to the bandwidth of the original system. Accordingly gain crossover and bandwidth are quite closely related.
In my designs I will focus more on gain crossover frequency assuming that higher gain crossover implies faster response.
Frequency Response
Section: 4
Bandwidth

## Slide 90: A quintessential dichotomy
The input will include disturbances. The system at least partially rejects the disturbances if their frequency components lie outside the closed-loop system bandwidth.
The bandwidth indicates the maximum frequency to which the system can react, i.e. the speed of response. A system with higher bandwidth reacts to higher frequencies, i.e. reacts quickly. As a result such a system may be expected to have a fast rise time and short settling time.
A quintessential dichotomy: speed of response calls for large bandwidth; disturbance rejection calls for small bandwidth.
Section: 4
Frequency Response

## Slide 91
Second Order System
Section: 4
Frequency Response
Phase margin (in degrees) vs z (blue) and linear approximation (red)
Bandwidth/natural frequency vs z.

## Slide 92: Note
The second formula suggests that large bandwidth implies large natural frequency. As real part = - zwn it follows that, for given z, large bandwidth implies dominant poles (and therefore all poles) far into LHP. This of course implies fast response as claimed above.
These formula are very approximate. We must use with great caution.
Section: 4
Frequency Response

## Slide 93
Second Order System
Section: 4
Frequency Response
Gain crossover/natural frequency vs z.

## Slide 94
Example 4.5
Section: 4
Frequency Response
I wish to vaguely justify or at least validate some of these formulae. To that end consider the following open-loop transfer function:
When placed in a unity negative feedback loop the resulting closed-loop transfer function becomes:

## Slide 95
Example 4.5
Section: 4
Frequency Response
So the closed-loop system is a canonical second order system with natural frequency if 1 rad/sec and damping ratio of 0.575. The approximate formulae now suggest:

## Slide 96
Example 4.5
Section: 4
Frequency Response
Use of Matlab’s margin command shows that these estimates are essentially spot on in this case.

## Slide 97: Example 4.5
Of course the point is that I can use these estimates in reverse. If the open-loop system has a phase margin of 57.5o and a gain crossover frequency of 0.7332 rad/sec then I deduce that the closed-loop system (where I assume unity negative feedback) will behave like a second order system having a damping ratio of 57.5/100 = 0.575 and a natural frequency given by:
Section: 4
Frequency Response

## Slide 98
Example 4.5
Section: 4
Frequency Response
Such a system will have:

## Slide 99
System Type
Section: 4
Frequency Response
Transfer function from r(t) to e(t)

## Slide 100
System Type
Section: 4
Frequency Response
Three most common kinds of reference input are
the step, (ii) the ramp and (iii) the parabola.
The error for these three reference inputs is:

## Slide 101
System Type
Section: 4
Frequency Response
A system is of type 0 if Go(s) has no poles at 0. In this case the steady-state errors for the three standard reference inputs appear to be:
A system of type 0 cannot track any of the three references
with zero error, but it can at least track the step with
finite error:

## Slide 102: Note
Actually the latter two are not infinity, but the simple linear theory cannot calculate them. All that can be said with some certainty is that they are not zero.
The finite error to a step input may be small if the DC gain of the open loop system is large.
Kp is the error constant for type 0 system. I find this notation appalling as it can readily be confused with proportional gain, but unfortunately it is standard.
Section: 4
Frequency Response

## Slide 103
System Type
Section: 4
Frequency Response
A system is of type 1 if Go(s) has a simple pole at 0. In this case the steady-state errors for the three standard reference inputs appear to be:
where Do(s) = sDo’(s). A system of type 1 tracks a step
input with zero error, cannot track a parabola and tracks a
ramp with finite error :

## Slide 104
System Type
Section: 4
Frequency Response
A system is of type 2 if Go(s) has a pole of multiplicity 2 at 0. In this case the steady-state errors for the three standard reference inputs are:
where Do(s) = s2Do’(s). A system of type 2 tracks a step
and ramp input with zero error, tracks a parabola input with
finite error :

## Slide 105: System Type and Bode Plots
Frequency Response
Section: 4
From above, the low frequency asymptote is a line with a slope of -20q dB per decade. The slope of this line therefore tells us q, the order of the pole at zero. But the system type is q.

## Slide 106: System Type and Bode Plots
Frequency Response
Section: 4
At w = 1, low freq. asymptote:
If q = 0 this const. is 20log10(Go(0))
If q = 1 this const. is 20log10(No(0)/Do'(0))
If q = 2 this const. is 20log10(No(0)/Do' (0))

## Slide 107: Note
It follows that the value of the low freq. asymptote at w = 1 permits us to find the error constant.
Section: 4
Frequency Response

## Slide 108: Example 4.6
Frequency Response
Section: 4
System type: 2
Relative degree: 3
Error constant Ka : 2

## Slide 109: Note
Low-freq asymptote slope = -40 dB/decade: system type = 2.
High-freq asymptote slope = -60 dB/decade: relative degree = 3.
Low-freq. asymptote value at w = 1 is: approx. 6 dB. Hence No(0)/Do'(0) approx. 2.
Hence Ka = 2 (approx.)
Section: 4
Frequency Response

## Slide 110
Section 4 - Conclusion
Section: 4
Frequency Response
The response of a closed loop system is partly determined by the frequency response and in particular by the phase margin and the closed-loop gain crossover frequency.
The Nyquist plot and the Bode plots are tools which can be employed in the design of controllers. The objective of the design is to “shape” the frequency response, generally to achieve a desired PM and commonly to achieve a desired gain crossover frequency.