## Slide 1
Control Systems
Stage 4: Electrical, Electronic and Communications Engineering
Dr Paul Curran
Room 145, Engineering.
paul.curran@ucd.ie
+353-1-7161846

## Slide 2: Overview of Topics
Mathematical background and problem statement.
Dominant pole placement via root locus.
Basic loop shaping.
Linear state feedback and observers.
Digital control.

## Slide 3
Section 5 - Outline
Lead Controllers.
Lag Controllers.
Lead/Lag Controllers.
Section: 5
Lead/Lag

## Slide 4
Frequency Domain Design
Section: 5
Lead/Lag
The real substance of this next section of the module is a discussion of a second design method, the frequency domain design method. This method is quite distinct from our previous method, the time domain or root locus design method, because it does not employ the idea of poles, but rather the idea of frequency response.

## Slide 5
Frequency Domain Design
Section: 5
Lead/Lag
To express that another way, we design, not with the aim of achieving desired closed-loop pole or dominant pole locations, but rather with the aim of “shaping” the open-loop frequency response in order to achieve desired levels of gain margin, phase margin, gain crossover frequency, etc.
Note an important phrase there, open-loop. The stability margins are determined by the open-loop frequency response and it proves to be far more straightforward to shape the open-loop, as distinct from the closed-loop, frequency response.

## Slide 6
Frequency Domain Design
Section: 5
Lead/Lag
A particularly significant aspect of the frequency domain analysis methods presented in the previous sections is that they do not change substantially in the presence of delay. A particularly significant aspect of the time domain analysis methods (those based on pole locations) is that they utterly transform in the presence of arbitrary levels of delay (with the number of poles jumping to infinity).
We find that frequency domain design methods are also well able to cope with delay, whereas time domain design methods become virtually useless.

## Slide 7
Frequency Domain Design
Section: 5
Lead/Lag
We can, and will, use frequency domain design methods to design P, PI, PID and other controllers.
Partly for historical reasons, but mainly because they more naturally lead to the discovery of how to shape the frequency response, we will introduce frequency domain design as a method for the design of two new types of controller, lead and lag controllers.
These controllers give us another bow in our quiver, so to speak. Sometimes a control problem just cannot be solved with a PID controller. It is good to have other options for when they are needed.

## Slide 8
Lead Controller
Section: 5
Lead/Lag
A lead controller has transfer function:
Peak phase:
Freq. of peak phase:
Gain at this freq:

## Slide 9
Effect of Lead Controller
Section: 5
Lead/Lag
Consider plant:
and lead controller:
The gain crossover frequency is higher and the phase is increased over a range of frequencies, so the phase margin may be increased.

## Slide 10
Frequency Domain Design
Section: 5
Lead/Lag
We see that the lead controller has increased the gain by a fixed amount at high frequencies, but left it unchanged at low frequencies. On the other hand it has increased the phase in a mid-range of frequencies but left it unchanged at lower and higher frequencies. Because of the lifting of the gain, the gain crossover frequency is generally higher. Because of the lifting of the phase in the mid-range (a range which generally includes the new gain crossover frequency) the phase margin is generally increased.

## Slide 11
Basic Idea of Lead Controller Design
Section: 5
Lead/Lag
Increase gain crossover frequency by introduction of positive gain at higher frequencies. Achieve desired phase margin by introduction of suitable positive phase at appropriate frequency.
Increased gain crossover frequency suggests improved speed and increase in phase margin suggests improved overshoot in closed-loop system.

## Slide 12
Example 5.1
Section: 5
Lead/Lag
Consider a simple plant:
Suppose we require zero steady-state error to a step input. We must include an integrator in the forward loop. Going ahead and including this we are left with an augmented plant:

## Slide 13
Example 5.1
Section: 5
Lead/Lag
The augmented plant has the following stability margins:

## Slide 14
Example 5.1
Section: 5
Lead/Lag
At about 21o the phase margin is fairly low. It would roughly correspond to the performance of a canonical second order system with a damping ratio of about 0.21. This would be expected to give a rather large overshoot of about 51%
The gain crossover frequency, at 0.682 rad/sec, is also fairly low. Given a damping ratio of 0.21 it suggests a natural frequency of about 0.71 rad/sec and a 2% settling time of about 1/((0.21)(0.71)) which is about 26 sec. Of course these are possibly dreadful approximations but they do give us some reason to believe that the system will have significant overshoot and long transient time.

## Slide 15
Example 5.1
Section: 5
Lead/Lag
The actual closed-loop step response (when the augmented plant is placed in a unity negative feedback loop) confirms these concerns. PO = 54.3%, ts(2%) = 30.9 sec.

## Slide 16
Example 5.1
Section: 5
Lead/Lag
Of course the reason for this terrible degradation in performance is that the introduction of the pole at zero has pulled the root locus towards the imaginary axis, slowing down the response considerably. This is why we have always argued that one never employs I-control.
I will demand improved performance by specifying a slightly higher phase margin and a higher gain crossover frequency. Specifically I will ask for a phase margin of 30o and a gain crossover frequency of 2 rad/sec.

## Slide 17
Example 5.1
Section: 5
Lead/Lag
So what will it take to achieve this? Well the Bode plot of the augmented plant reveals that at the desired new gain crossover frequency of 2 rad/sec the gain of the augmented plant is -20 dB and the phase is -217o.

## Slide 18
Example 5.1
Section: 5
Lead/Lag
If I place a controller Gc(s) in series with the augmented plant then I have:

## Slide 19
Example 5.1
Section: 5
Lead/Lag
Putting in known results:
Now for 2 rad/sec to actually be the new gain crossover frequency I require that the open-loop gain should be 0 dB at this frequency.

## Slide 20
Example 5.1
Section: 5
Lead/Lag
If 2 rad/sec is thus made to be the new gain crossover frequency then for the phase margin to be 30o I require that the open-loop phase should be -150o or more at this frequency. In short:

## Slide 21
Example 5.1
Section: 5
Lead/Lag
So the controller must introduce a gain of 20 dB and a phase of at least 67o at 2 rad/sec. Well a lead controller introduces a positive phase over a specified range of frequencies. The maximum amount of phase introduced depends only on the parameter a and the frequency at which this phase occurs depends upon both parameters a and t. It seems that a lead controller can give any specified amount of positive phase (up to 90o maximum) at any specified frequency. But it then gives at this frequency whatever gain it gives. As I have defined it a lead controller does not offer enough flexibility to see the job done. I circumvent this little detail by employing a proportional gain in series with a lead controller.

## Slide 22
Example 5.1
Section: 5
Lead/Lag
So the “lead plus proportional gain” controller must introduce a gain of 20 dB and a phase of at least 67o at 2 rad/sec. One standard way to design a controller of this kind is to demand that the controller give a peak phase of the required 67o at 2 rad/sec and that it give a gain of 20 dB at this frequency, i.e.

## Slide 23: Note
Evidently we are left with three equations in three unknowns. As long as the required peak phase is positive and does not exceed 90o we can in principle solve. Actually we will run into some difficulty as the required peak phase becomes very nearly equal to (i.e. slightly less than) 90o for this will require very large values of a and fabrication may be difficult. Many other problems may also arise because of the linear approximation always hanging there in the background. As quantities become large we simply do not remain close to the desired operation point and the nonlinear terms make there presence felt.
Section: 5
Lead/Lag

## Slide 24
Example 5.1
Section: 5
Lead/Lag

## Slide 25
Example 5.1
Section: 5
Lead/Lag
The phase margin and gain crossover frequency are almost exactly as required. The discrepancy is because of the selection of simpler approximate values for the controller parameters.

## Slide 26
Example 5.1
Section: 5
Lead/Lag
The resulting step response has zero steady-state error but with significantly improved overshoot of 36.2% and dramatically improved 2% settling time of 6.55 sec.

## Slide 27
Lag Controller
Section: 5
Lead/Lag
A lag controller has transfer function:
Min. phase -F:
Freq. of min. phase:
Gain at this freq:
Gain at high freq:

## Slide 28
Lag Controller Design
Section: 5
Lead/Lag
By selecting sufficiently large proportional gain k the error constant can be reduced below any desired target value. But the resulting closed loop system is commonly less stable since the gain crossover frequency has typically been increased and the phase margin reduced. The purpose of a lag controller is to restore the phase margin to acceptable values thereby permitting recovery of stability without affecting the benefit of the proportional gain, namely reduced steady state error. A price paid is commonly speed of response.
The error constant for a step input is:

## Slide 29
Example 5.2
Section: 5
Lead/Lag
Require a steady-state error to a step input below 5% Achieve reduction by introducing proportional gain k.
Consider a very simple plant:
So the steady-state requirement is achieved by using a proportional gain of about 10.

## Slide 30
Example 5.2
Section: 5
Lead/Lag
We see that the proportional gain has a detrimental effect upon the closed-loop stability if the system is placed in a unity negative feedback loop.
Plant+Gain
Plant

## Slide 31
Lag Controller Design
Section: 5
Lead/Lag
The effect of the proportional gain upon the Bode plots is none at all for the phase plot and the raising of the magnitude plot by the fixed value of
The new gain crossover frequency is where the plant itself has a gain of -20 dB, and this is higher than the gain crossover frequency of the plant itself. This means that the phase margin is determined from a higher frequency where it has declined.

## Slide 32
Lag Controller Design
Section: 5
Lead/Lag
It may be that the “new” gain crossover frequency is now either unnecessarily or unbelievably high. The problem is that systems are always subject to disturbances. These disturbances, being somewhat noisy, have high frequency components. To reject disturbances therefore you do not wish to have a system which is capable of reacting at unnecessarily high frequencies. So in the case of control systems there is such a thing as too fast, and not just because it stretches the credibility of the model. A system should be as fast as it needs to be and no faster. Such a system will better manage the very difficult compromise required of control systems: to react promptly to control inputs and to reject disturbances.

## Slide 33
Lag Controller Design
Section: 5
Lead/Lag
A lag controller reduces the gain at higher frequencies. It will therefore reduce the gain crossover frequency, bringing it back towards its original value. In this way the lag controller can somewhat restore the original phase margin while returning the speed of response to appropriate levels.
To illustrate suppose we require a phase margin of 60o and a gain crossover frequency somewhat closer to the original value but otherwise unspecified.

## Slide 34
Example 5.2
Section: 5
Lead/Lag
First we find the frequency, w0 , at which the phase of the plant + proportional gain is approximately -180o + PMdesired , i.e. about -120o. The design method here will prove to be approximate so we incorporate a safety margin of about 5o, i.e. we look for the frequency at which the phase is about -115o.
w0 = 1.56 rad/sec
Gain at 1.56 rad/sec is 15.2 dB

## Slide 35
Example 5.2
Section: 5
Lead/Lag
We design the lag controller so that this frequency, 1.56 rad/sec, lies in the high frequency range of the system. The high frequency range starts at 10/t according to the Bode approximations. So we require t = 10/w0 = 6.41 sec. Now, if this frequency is made equal to the gain crossover frequency, then by definition the phase margin will be approximately the desired phase margin of 60o since the high frequency phase of the lag controller is zero so that the open-loop phase equals the phase of the plant + proportional gain at this frequency and by definition of the frequency that is about -120o.

## Slide 36
Example 5.2
Section: 5
Lead/Lag
So the final part of the design is to ensure that 1.56 rad/sec actually is the new gain crossover frequency. I note that this is still higher than the gain crossover frequency of the original plant. We require:

## Slide 37
Example 5.2
Section: 5
Lead/Lag
Of course we have ensured that the frequency of 1.56 rad/sec is in the high frequency range of the lag controller. It follows that the gain of the controller at this frequency is approximately equal to the high frequency gain:

## Slide 38
Example 5.2
Section: 5
Lead/Lag
Achieved PM is 60.2o very close to desired value. The achieved gain crossover frequency is 1.57 rad/sec, almost exactly the target value.
Notes: Desired PM nearly achieved, gain crossover close indeed to required value.

## Slide 39
Example 5.2
Section: 5
Lead/Lag
Resulting step response shows desired steady state error is achieved with a relatively low PO of about 4.25% and a rather long 2% settling time of about 15.4 sec.
Note that the rise-time is short, so the system is rather quick. In spite of this the settling time is very long because of the long time constant of the lag controller. This type of response is typical of this control method.

## Slide 40
Example 5.3
Section: 5
Lead/Lag
For error constant Kv > 160 need proportional gain, k, in series with plant k/36 > 160, i.e. k > 5,760 which renders system unstable.
Unstable for k > 4800
approx.

## Slide 41
Lag + P Controller
Section: 5
Lead/Lag
The DC gain is k which may be chosen large to ensure good steady-state performance, but the high frequency gain is k/a which may be chosen small so that stability is not compromised. eg.
stable for 0 < k < 9100. Has nearly doubled range of stability at no cost to DC gain.

## Slide 42
Example 5.3
Section: 5
Lead/Lag

## Slide 43
Example 5.3
Section: 5
Lead/Lag
Let k = 6000.
Bode plot of 6000Gp shown. Alternatively can work out from Bode plot of Gp. Note degradation in stability margins and massive increase in gain crossover frequency.

## Slide 44
Example 5.3
Section: 5
Lead/Lag
Require phase margin of 60o. Consider where the phase of the augmented plant is a little over 60o above -180o. Say where the phase is about -110o. This occurs at a frequency of about 10 rad/sec. A gain crossover frequency of 10 rad/sec would be far more reasonable than a gain crossover of over 66 rad/sec. We elect to achieve a gain crossover frequency of 10 rad/sec. For this to equal the gain crossover frequency I require:
Gain of controller @ 10 rad/sec + Gain of augmented plant @ 10 rad/sec = 0 dB.

## Slide 45
Example 5.3
Section: 5
Lead/Lag
The gain of the augmented plant at 10 rad/sec is about 24 dB. Accordingly the gain crossover frequency is about 10 rad/sec if the gain of the controller at 10 rad/sec equals -24 dB. For the phase margin of the system to exceed about 60o we require:
Phase of controller @ 10 rad/sec + Phase of augmented plant @ 10 rad/sec ≥ -120o.

## Slide 46
Example 5.3
Section: 5
Lead/Lag
A way to achieve this is to require that 10 rad/sec is in the high frequency region of the lag controller, i.e.
As the phase of the augmented plant at 10 rad/sec is about -110o (this is how we chose the frequency of 10 rad/sec) we simply require that the phase of the controller be greater than about -10o.
Of course the controller gain then equals the high frequency gain and this should equal -24 dB, i.e.

## Slide 47
Example 5.3
Section: 5
Lead/Lag

## Slide 48: Note
A disadvantage of this method of designing a lag controller (i.e. by requiring that a certain frequency should lie in its high frequency region) is that the required time constant of the lag controller is commonly rather high, so that the speed of response of the resulting closed loop system is in general expected to be slow. This commonly takes the form of a fairly quick settling to within 5 or 10% of the steady state, but a sluggish convergence thereafter.
Section: 5
Lead/Lag

## Slide 49: Note
Accordingly I do not strongly recommend this method of lag controller design, although it is fairly popular in textbooks and on websites. I cover it because it offers a further illustration I think of some of the basic ideas of loop shaping using lead, lag and lead-lag controllers. It really only works when the specification on the performance is not overly concerned with speed of response or gain crossover frequency and I have to say that is, in my opinion, a fairly academic problem.
Section: 5
Lead/Lag

## Slide 50
Example 5.4
Section: 5
Lead/Lag
Design a lead-lag + P controller to meet the following specification:
Zero steady-state error for step input.
Steady-state error for ramp input less than 8.5%
Percentage overshoot not exceeding 15%
2% settling time not exceeding 3 sec.

## Slide 51
Example 5.4
Section: 5
Lead/Lag
Plant has pole at zero so first spec. automatically met.
Second spec. met by proportional controller with gain k such that
Let k = 48.

## Slide 52
Example 5.4
Section: 5
Lead/Lag
Third spec. requires z > 0.517,
i.e. PM > 51.7o
Let PM = 60o or more, i.e. z > 0.6
Fourth spec. requires wn > 2.22 rad/sec,
i.e. wgc > 1.3 rad/sec.
Let wgc = 1.8 rad/sec. or more allowing if the resulting controller time constants are too high.

## Slide 53
Example 5.4
Section: 5
Lead/Lag
Note proportional gain has compromised stability.

## Slide 54
Example 5.4
Section: 5
Lead/Lag
Phase at 1.8 rad/sec is
-175o approx.
Gain at 1.8 rad/sec is 9.36 dB approx.

## Slide 55
Example 5.4
Section: 5
Lead/Lag
For gain crossover to occur at 1.8 rad/sec require:
Gain of lag + Gain of lead = -9.36 dB approx at 1.8 rad/sec.
For PM of 60o or more require:
Phase of lag + phase of lead = 55o or more at 1.8 rad/sec.

## Slide 56
Example 5.4
Section: 5
Lead/Lag
Achieved by:
Gain of lag = -20log10(alag) at 1.8 rad/sec.
Gain of lead = -9.36+ 20log10(alag) dB at 1.8 rad/sec.
Phase of lag approx 0o at 1.8 rad/sec.
Phase of lead = 55o or more at 1.8 rad/sec.
i.e. assume that 1.8 rad/sec is in high frequency region as far as lag controller is concerned.

## Slide 57
Example 5.4
Section: 5
Lead/Lag
give phase of lead = 52o at 1.85 rad/sec.
Also gives gain of lead at 1.8 rad/sec =

## Slide 58
Example 5.4
Section: 5
Lead/Lag
Finally for 1.8 rad/sec to be in high frequency range of lag controller require:
although this is almost certainly too high.

## Slide 59
Example 5.4
Section: 5
Lead/Lag
Note that gain crossover is as required but that PM is less than the 60o sought, although more than the 51.7o apparently needed.

## Slide 60
Example 5.4
Section: 5
Lead/Lag
Note achieved value of PO as required. Achieved value of settling time quite poor due to lag time constants.

## Slide 61
Example 5.4
Section: 5
Lead/Lag
Third spec. requires z > 0.517,
i.e. PM > 51.7o
Let PM = 60o or more, i.e. z > 0.6
Fourth spec. requires wn > 2.22 rad/sec,
i.e. wgc > 1.3 rad/sec.
Let wgc = 2.5 rad/sec.
Try again with more aggressive over compensation of fourth spec.

## Slide 62
Example 5.4
Section: 5
Lead/Lag
Phase at 2.5 rad/sec is
-190o approx.
Gain at 2.5 rad/sec is 3.49 dB approx.

## Slide 63
Example 5.4
Section: 5
Lead/Lag
For gain crossover to occur at 2.5 rad/sec require:
Gain of lag + Gain of lead = -3.49 dB approx at 2.5 rad/sec.
For PM of 60o or more require:
Phase of lag + phase of lead = 70o or more at 2.5 rad/sec.

## Slide 64
Example 5.4
Section: 5
Lead/Lag
Achieved by:
Gain of lag = -20log10(alag) at 2.5 rad/sec.
Gain of lead = -3.49+ 20log10(alag) dB at 2.5 rad/sec.
Phase of lag approx 0o at 2.5 rad/sec.
Phase of lead = 70o or more at 2.5 rad/sec.
i.e. assume that 2.5 rad/sec is in high frequency region as far as lag controller is concerned.

## Slide 65
Example 5.4
Section: 5
Lead/Lag
gives phase of lead = 70o at 2.5 rad/sec.
Also gives gain of lead at 2.5 rad/sec =

## Slide 66
Example 5.4
Section: 5
Lead/Lag
Finally for 2.5 rad/sec to be in high frequency range of lag controller require:
although this is almost certainly too high.

## Slide 67
Example 5.4
Section: 5
Lead/Lag
Note that gain crossover is as required but that PM is less than the 60o sought, although more than the 51.7o apparently needed.

## Slide 68
Example 5.4
Section: 5
Lead/Lag
Note achieved value of PO as required. Achieved value of settling time still quite poor but at least improved. 5% settling time is quite short.

## Slide 69
Example 5.4
Section: 5
Lead/Lag
Phase at 2.5 rad/sec is -190o approx.
Gain at 2.5 rad/sec is 3.49 dB approx.
Since the lag introduces this annoying effect of a long drawn out final convergence to steady state, why use the lag at all?

## Slide 70
Example 5.4
Section: 5
Lead/Lag
For gain crossover to occur at 2.5 rad/sec require:
Gain of controller = -3.49 dB approx at 2.5 rad/sec.
For PM of 60o or more require:
Phase of controller = 70o or more at 2.5 rad/sec.
A lead controller (or any number of them) cannot introduce negative gain, so this problem cannot be solved by lead controllers alone.

## Slide 71
Example 5.4
Section: 5
Lead/Lag
The main lesson here is that when loop shaping we can hit our targets exactly, i.e. get the desired PM and gain crossover frequency but find that the precarious relationship between these quantities and the step response results in a step response which does not accord with what we required.

## Slide 72
Example 5.5
Section: 5
Lead/Lag
I stated at the outset that this section was really about a design method, not about the design of particular types of controllers. To illustrate this point let me apply this method to the design of a PID controller. Consider plant:
The step response shows that the steady-state error is 25% , the 2% settling time is 4.2 sec and there is no overshoot.

## Slide 73
Example 5.5
Section: 5
Lead/Lag
I adopt the following specifications:
Zero steady state error to step input,
2% settling time less than 2 sec,
percentage overshoot less than 2%
The first specification calls for the introduction of an integerator in the forward loop, i.e. an I-term in the controller.
I must translate the remaining two specifications into specifications on phase margin and gain crossover frequency.

## Slide 74
Example 5.5
Section: 5
Lead/Lag
Assuming that the resulting closed-loop system will have a dominant pair, the third specification requires the damping ratio of this pair to be about 0.8 or more, i.e. PM ≥ 80o.
Assuming that the resulting closed-loop system will have a dominant pair, the second specification then requires the natural frequency, ωn , to be about 2.5 rad/sec or more, i.e.

## Slide 75
Example 5.5
Section: 5
Lead/Lag
Plant gain at 2 rad/sec = -10.6 dB
Plant phase at 2 rad/sec = -90.2o

## Slide 76
Example 5.5
Section: 5
Lead/Lag
Require gain of controller at 2 rad/sec = 10.6 dB so that 2 rad/sec actually equals gain crossover frequency.
Require phase of controller at 2 rad/sec > -9.8o so that PM is approx. 80o.
Of course, if we employ a PI controller, then at 2 rad/sec we have:

## Slide 77
Example 5.5
Section: 5
Lead/Lag
Require phase of 2j + z > 80.2o = 1.4 rad, so that
Try z = 0.3. Require:

## Slide 78
Example 5.5
Section: 5
Lead/Lag
Meets frequency spec. but fails original spec. being too slow.

## Slide 79
Example 5.5
Section: 5
Lead/Lag
To speed up response look to achieve a much higher gain crossover frequency of 6 rad/sec. while still requiring PM ≥ 80o.
Plant gain at 6 rad/sec = -23.3 dB
Plant phase at 6 rad/sec = -137o

## Slide 80
Example 5.5
Section: 5
Lead/Lag
Require gain of controller at 6 rad/sec = 23.3 dB so that 6 rad/sec actually equals gain crossover frequency.
Require phase of controller at 6 rad/sec > 37o so that PM is approx. 80o.
Of course, if we employ a PI controller, then at 6 rad/sec we have:
which has a maximum phase of 0o. The higher gain crossover frequency cannot be achieved with a PI controller.

## Slide 81
Example 5.5
Section: 5
Lead/Lag
I must choose a PID controller so that at 6 rad/sec I have:
Require phase of (6j+z1)(6j+z2) > 127o. I can achieve this by asking for each of the factors to introduce a phase of about 65o =1.13 rad, i.e. try z1 = z2= z:

## Slide 82
Example 5.5
Section: 5
Lead/Lag
Try z = 2.8. Require:

## Slide 83
Example 5.5
Section: 5
Lead/Lag
Meets frequency spec. but fails to meet original spec. having overshoot of 6.32%

## Slide 84
Example 5.5
Section: 5
Lead/Lag
Require phase of (6j+z1)(6j+z2) > 127o. I can achieve this by asking for 45o phase from the first factor and 82o = 1.43 rad from the second, i.e. z1 = 6 and :
In retrospect the double zero was not a good idea. Zeros tend to introduce overshoot, double zeros even more so.

## Slide 85
Example 5.5
Section: 5
Lead/Lag
Try z2 = 0.8. Require:

## Slide 86
Example 5.5
Section: 5
Lead/Lag
Meets frequency spec. and meets original spec.

## Slide 87
Example 5.5
Section: 5
Lead/Lag
Achieved steady-state error is zero.
Achieved PO is 1.09% < 2%
Achieved 2% settling time is 0.447 sec < 2 sec.

## Slide 88
Example 5.6
Section: 5
Lead/Lag
We consider a last example with a view to reinforcing the claim for two advantages of the frequency domain design methodology, namely that we can employ experimental frequency response data (as distinct from a model) and that the system may incorporate delay.
Accordingly consider the system:

## Slide 89
Example 5.6
Section: 5
Lead/Lag
I can draw the Bode magnitude and phase plots
Although we have the transfer function, suppose we did not. Suppose we only had the Bode plots.

## Slide 90
Example 5.6
Section: 5
Lead/Lag
Low frequency asymptote 0dB/dec: type 0.
High frequency asymptote -40dB/dec: rel. deg. = 2

## Slide 91
Example 5.6
Section: 5
Lead/Lag
Low frequency asymptote 0o: type 0.
High frequency asymptote not -180o: delay present.

## Slide 92
Example 5.6
Section: 5
Lead/Lag
With delay/latency L the correct form of the phase at high frequency becomes
As log10(ω) changes from 1 to 2 the phase drops from about -300o to -1400o. Magnitude plot suggest that ω = 10 is in high frequency region.

## Slide 93
Example 5.6
Section: 5
Lead/Lag
I obtain approximately
Giving the estimate:
Pretty good given the level of approximation in the estimates. The real lesson however is that when delay is present we require two phase plots, one log plot and one linear plot.

## Slide 94
Example 5.6
Section: 5
Lead/Lag
High frequency asymptote:
slope about (-1300+750)/50 = -11 = - 0.192(180/π).

## Slide 95
Example 5.6
Section: 5
Lead/Lag
2% settling time: 4.24 sec
PO: 54.8%
Steady-state error: 91.67%

## Slide 96
Example 5.6
Section: 5
Lead/Lag
I will make an ill-considered specification:
Zero steady-state error to step input
2% settling time not exceeding 2 sec
Percentage overshoot not exceeding 10%
Actually the 2% settling time constraint is preposterous.

## Slide 97
Example 5.6
Section: 5
Lead/Lag
Translate specifications:
Require I-term, i.e. open-loop pole at 0.
Require dominant pair with damping ratio exceeding 0.6. As there is 0.2 sec delay built in I aim for 2% settling time less than 1.8 sec giving natural frequency exceeding 3.7 rad/sec, i.e. PM = 60o or more and gain crossover frequency = 1.7 rad/sec or more.
Aim for PM ≥ 65o and ωgc ≥ 1.7 rad/sec.

## Slide 98
Example 5.6
Section: 5
Lead/Lag
PM ≥ 65o and ωgc ≥ 1.6 rad/sec.
Magnitude plot gives that plant gain at 1.7 rad/sec is -16.5 dB
Phase plot gives that plant phase at 1.7 rad/sec is -56.5o
Controller must introduce gain of 16.5 dB at 1.7 rad/sec and phase exceeding -58.5o , say -55o

## Slide 99
Example 5.6
Section: 5
Lead/Lag
The Bode plots shown are for the plant without the delay. The magnitude plot is unchanged when the delay is included.

## Slide 100
Example 5.6
Section: 5
Lead/Lag
With delay included the phase at 1.71 rad/sec is:

## Slide 101
Example 5.6
Section: 5
Lead/Lag
PM ≥ 65o and ωgc ≥ 1.6 rad/sec.
Controller must introduce gain of 16.5 dB at 1.7 rad/sec and phase exceeding -52.5o
At 1.7 rad/sec controller must have gain of 6.6834 or more, say 6.7.
At 1.7 rad/sec controller must have phase of say -50o = -0.87 radians or more.

## Slide 102
Example 5.6
Section: 5
Lead/Lag
If I use a PI controller (recall I require a pole at 0) then

## Slide 103
Example 5.6
Section: 5
Lead/Lag
implies
implies
We have designed a PI controller for a system incorporating delay by using frequency response data only. Does it work?

## Slide 104
Example 5.6
Section: 5
Lead/Lag
I achieve a gain-crossover frequency of 1.89 rad/sec, in excess of requirement.
I achieve a PM of about 57.8o slightly above the target value. So in these terms the answer is yes it does work.
The real question however is whether the resulting closed-loop system meets the step response specifications.

## Slide 105
Example 5.6
Section: 5
Lead/Lag
Basic Matlab is not the best platform on which to attempt to simulate the unit step response of a closed-loop system incorporating delay.
There are two approaches to solving this problem within the general Matlab environment:
(i) write an m-file employing one of the built-in differential equation solvers (eg ode45)
(ii) use Simulink

## Slide 106
Example 5.6
Section: 5
Lead/Lag
Simulink is a specialist dynamical system simulator with an easy-to-use graphical interface.
Notes: To “connect” to line use right mouse button.
Can also choose as sink “to workspace” in order to manipulate data in command window (eg print). In this case it is useful to use clock so that you also have timing information.
Scope is tricky to get right. Right-click on axes to adjust settings.
Need to go into simulation configuration settings to set max step size to 0.02 ti get nice smooth plot in this case.
Need to select array as save format for outputs to workspace tt and yy.

## Slide 107
Example 5.6
Section: 5
Lead/Lag
Simulink gives the following unit step response for our closed-loop system:
Steady-state error is zero, PO is rather small.
The 2% settling time is about 6 sec.

## Slide 108
Example 5.6
Section: 5
Lead/Lag
So essentially the answer is no, the closed-loop system does not meet the time-domain specifications. Of course I can redesign, aiming for a much higher gain crossover frequency and this should improve the speed of response. A first pass in design seldom, if ever, solves the problem. This failure does not however undermine the main point. We have undertaken this design by employing the frequency response data only.

## Slide 109
Example 5.6
Section: 5
Lead/Lag
I can offer some explanation for my failure. The root locus of the latency-free part of the open-loop transfer function shows a dominant pole between 0 and the system zero at -1.
The associated closed-loop pole cannot be fast enough and when latency is present it will surely be slower still.

## Slide 110
Example 5.7/3.4: PI Controller
Section: 6
Lead/Lag

## Slide 111: Example 5.7/3.4
Suppose the specification of performance is as follows.
The system should track a step input with zero error.
The 2% settling time should be about 2 sec or better.
The overshoot should not exceed 5%
Section: 6
Lead/Lag

## Slide 112
Example 5.7/3.4: PI Controller
Section: 6
Lead/Lag

## Slide 113: Example 5.7/3.4
Integrator in forward loop.
The overshoot should not exceed 5% implies damping ratio of about 0.7, i.e. PM = 70o.
The 2% settling time should be about 2 sec or better, given required damping ratio requires a natural frequency of about 2.86 rad/sec, i.e. gain crossover frequency of about 1.9 rad/sec using
Section: 6
Lead/Lag

## Slide 114
>> Gp = tf([1],[1 12 32])
>> Gint = tf([1],[1 0] add integrator
>> Gpa = series(Gp,Gint)
>> margin(Gpa) draw Bode plot
Section: 6
Example 5.7/3.4
Lead/Lag
The current PM is fine but the gain crossover frequency is far too low. This is reflected in a settling time of 124 sec of current closed-loop system.

## Slide 115
>> bode(Gpa) draw Bode plot
Section: 6
Example 5.7/3.4
Lead/Lag
Gain at 1.9 rad/sec is about -37dB and the phase is about -129o.

## Slide 116
Example 5.7/3.4
Section: 6
Lead/Lag
Gain of residual controller @ 1.9 rad/sec – 37 dB = 0 dB
For the new gain crossover frequency to actually equal 1.9 rad/sec require:
where the residual controller refers to what is left after the integrator has been absorbed into the augmented plant, i.e. to k(s+z).
For the new phase margin to exceed 70o require:
Phase of residual controller @ 1.9 rad/sec –129o ≥ – 110o

## Slide 117
Example 5.7/3.4
Section: 6
Lead/Lag
Gain of residual controller @ 1.9 rad/sec = 37 dB
Phase of residual controller @ 1.9 rad/sec ≥ 19o
try

## Slide 118
>> Gc = tf(13.24*[1 5],[1 0])
>> Go = series(Gp,Gc)
>> margin(Go)
Section: 6
Code
Lead/Lag
Gain crossover frequency is at 1.94 rad/sec and PM is 71.7o, slightly better than required.

## Slide 119
>> Gcl = feedback(Go,Gideal)
>> step(Gcl)
>> stepinfo(Gcl)
Section: 6
Code
Lead/Lag
RiseTime: 0.7747
SettlingTime: 1.1965
SettlingMin: 0.9001
SettlingMax: 1.0101
Overshoot: 1.0119
Undershoot: 0
Peak: 1.0101
PeakTime: 1.6992

## Slide 120
Example 5.7/3.4
Section: 6
Lead/Lag
So the specifications are met. Frequency-domain methods, i.e. loop shaping offers a genuine alternative to root locus-based methods.

## Slide 121: Overview of Topics
Models and Block Diagrams:
Pole locations and Transient Response.
PID Controllers and Root Locus Design.
Frequency Response Analysis and Design.
State Space Models:
Pole Placement and Observer Design.
Digital Control.

## Slide 122
State Space
Section: 6
State Space
The state-space representation of a system takes the form
of the following very general equations
The vector x is nx1 and is called the state vector.
The matrix A is nxn and is called the state transition matrix.
The vector u is mx1 and is called the input vector (or input).
The vector y is lx1 and is called the output vector (or output).
In the special case m = 1, l = 1 the system is SISO.

## Slide 123
Example 6.1: Magnetically suspended ball
Section: 6
where h is the vertical position (measured down from a reference) of the ball, i is the current through the electromagnet, V is the applied voltage, M is the mass of the ball, g is gravity, L is the inductance, R is the resistance and K is a coefficient that determines the magnetic force exerted on the ball. For simplicity, we will choose values
M = 0.05 kg, K = 0.0001, L = 0.01 H, R = 1, g = 9.81 m/sec2 .
State Space

## Slide 124
Example 6.1: Magnetically suspended ball
Section: 6
The system is at equilibrium (the ball is suspended in midair)
whenever all of the quantities in the system are static, i.e.
when
State Space
Assume h = 0.01 m at equilibrium, i.e. V = 7V approx.

## Slide 125
Example 6.1: Linearisation
Section: 6
Offset variables
State Space
Equilibrium equations

## Slide 126
Example 6.1: Linearisation
Section: 6
State Space

## Slide 127
Example 6.1: Linearisation
Section: 6
State Space

## Slide 128
Example 6.1: Linearisation
Section: 6
State Space
definition of state vector

## Slide 129
Example 6.1: Linearisation
Section: 6
State Space
Regarding the offset of h as the output, offset of voltage V
as input and replacing parameters by their known values
we obtain the standard state equation

## Slide 130
State Space Poles
Section: 6
If, as claimed above, the state-space representation is an
alternative but equivalent representation to the transfer
function then something must play the vital role of the
system poles within this representation. This is, of course,
the case and the “something” in question is the set of
eigenvalues of the state transition matrix A. If the
closed-loop system has state-space representation
State Space
then the closed-loop transfer function is

## Slide 131
State Space Poles
Section: 6
State Space
characteristic polynomial of A. It is of
degree n and its roots are the eigenvalues of A.
Everything that we have ever said about desirable pole
locations may be immediately translated into assertions
concerning desirable eigenvalue locations.

## Slide 132
Example 6.1: Poles
Section: 6
State Space
One of the first things to do with the state equations is to
find the open-loop poles of the system and these are the
eigenvalues of the state transition matrix A. For the ball and
magnetic field:
poles =
31.3050
-31.3050
-100.0000
>> eig(A)
Notes: One of the poles is in the right half plane, which means that the open-loop system is unstable. This is hardly surprising. A ball does not tend as a rule to float in mid air.
To check out what happens to this unstable system when there is a nonzero initial condition:
t = [0:0.01:2]; u = 0*t; x0 = [0.005 0 0]; [y,x] = lsim(A,B,C,0,u,t,x0); h = x(:,2); plot(t,h)
It seems that the distance between the ball and the electromagnet will go to infinity. Actually of course it will not (the earth is finite after all and it is hardly going to leave it). In fact either the ball will hit the table/floor resulting in an entirely different unmodelled behaviour or the offset from equilibrium grows to a point where the linearization is simply not a good enough approximation and any predictions based upon it become unreliable.

## Slide 133
Example 6.1: Poles
Section: 6
State Space
One of the poles is in the right half plane, which means that the open-loop system is unstable. This is hardly surprising, a ball does not willing hover in mid-air. There are a number of ways of determining the step response, but the simplest is usually to use the ss command.
>> Gp = ss(A,B,C,D)
>> step(Gp)
Notes: .

## Slide 134
Example 6.1: Poles
Section: 6
State Space
Since h is measured downwards there is a problem here. It confirms instability, but it suggests that the ball will shoot up into the air. We may obtain the transfer function using the ss2tf command.
>> [Np,Dp]= ss2tf(A,B,C,D)
Dp =
1.0e+004 *
0.0001 0.0100 -0.0980 -9.8000
Np = 0 -0.0000 -0.0000 -280.0000
Notes: .

## Slide 135
State Space Poles
Section: 6
State Space
Matlab is suggesting that the transfer function is:
Matlab is wrong, the transfer function is:

## Slide 136
Example 6.1: Poles
Section: 6
State Space
On this occasion the lsim command does a better job.
>> Gp = ss(A,B,C,D)
>> T = [0:0.001:1];
>> U = zeros(1,length(T));
>> x0 = [0.0001;0;0];
>> lsim(Gp,U,T,x0)
Notes: .

## Slide 137
Pole Placement
Section: 6
The relationship between system poles and eigenvalues of
the state transition matrix, together with the approximate
analyses concerning the value of certain pole locations leads
to the first new design method that we shall consider:
pole placement. This is essentially a generalisation of the
root locus procedure.
In classical control it was assumed that the output was
available to be fed back. This is now called output feedback.
For the purposes of this problem we assume that the user
has gone to the extraordinary effort of measuring all of the
states of the system. The complete state vector x is now
available for feedback and we can therefore investigate
full-state linear feedback.
State Space

## Slide 138
Full-State Linear Feedback
Section: 6
Schematic:
State Space
Closed-loop characteristic polynomial =
Notes: Note we assume that the matrix D is zero as indeed it is in the case of the ball and magnetic field. I am also using unconventional notation, denoting the input of the plant e.
We have quite an amount of control over the nature of the roots of this closed-loop characteristic polynomial by virtue of our complete (in principle) control over the vector of feedback gains K. In the case of the ball and magnetic field and more generally in the case of a SISO plant the vector K is 1xn.
The pole placement design procedure amounts to choosing the desired locations for the closed-loop poles and then attempting to solve the algebraic problem of determining feedback gains to ensure that the closed-loop poles actually acquire these desired values. So, whereas the root locus procedure effectively places the dominant poles, the pole placement procedure places all of the poles.

## Slide 139
Example 6.1
Section: 6
Suppose the specifications for the controller performance are:
2% settling time less than 0.4 sec
Percentage overshoot less than 4.3%
State Space
We have three poles in this system, so to employ our
standard “specification to pole location” translation procedure
we will require that there exists a dominant pair of poles.
The percentage overshoot will require that the damping ratio
for this dominant pair exceed 0.7071. The 2% settling time will
then require that the natural frequency for this dominant pair
exceed 14.1421 rad/sec. The pair comprise the roots of the
quadratic:

## Slide 140
Example 6.1
Section: 6
The third pole must be real (obviously) and must be dominated
by the dominant pair. As the dominant pair have real part
= -10 the third dominated pole must have real part much less
than this. A choice of -50 is not an unreasonable first guess.
State Space
The place command places the closed-loop poles at
-10±10j, -50
yielding gains:
Notes: A simple ad hoc argument can also determine K but that is not important right now. The suggested K actually gives closed-loop poles:
-50.0001, -9.9999 +10.0000i, -9.9999 -10.0000i which are not quite what we wanted.
The 2% settling time is not much in excess of 0.4 sec if at all. The percentage overshoot is manifestly small. The big problem with the performance is that the steady-state error is very large since the closed-loop DC gain of -280/10000 =-0.028 is far from unity.

## Slide 141
Example 6.1: Poles
Section: 6
State Space
>> target_poles = [-10+10i;-10-10i;-50];
>> K = place(A,B,target_poles)
The achieved poles are the eigenvalues of A-BK, i.e.
>> eig(A-(B*K))
ans =
-50.0000
-10.0000 +10.0000i
-10.0000 -10.0000i
Notes: .

## Slide 142
Example 6.1
Section: 6
The closed-loop poles end up exactly where we required. The overshoot is fine as is the settling time. The steady state error is dreadful however.
State Space
The gains are also very fussy and there is a rather worrying sensitivity of the closed-loop pole locations to the third, smaller gain. Indeed the system is barely stable if this gain is reduced to -0.2.

## Slide 143
Tracking
Section: 6
We deal with the easy problem first. The tracking in the above example is dreadful. The problem is caused by the fact that in the full-state linear feedback schematic above we do not compare the output signal to the reference signal; instead we measure all of the states, multiply by the gain vector K and then subtract this result from the reference. So Kx tracks the reference, but as there is no reason to expect that Kx will strongly resemble the output y it cannot be expected that the output will thereby track the reference. This is a basic problem with full-state linear feedback as it has so far been presented.
To eliminate this problem we scale the reference input.
State Space

## Slide 144
Nbar
Section: 6
State Space

## Slide 145
Example 6.1
Section: 6
State Space
>> Nbar = -1/(C*inv(A-(B*K))*B)
>> Gcl = ss(A-(B*K),Nbar*B,C,D)
>> step(Gcl)

## Slide 146
Example 6.1
Section: 6
The steady state error has been fixed. The overshoot is fine. The settling time is a little off. Since a number of you have already discovered the command let us use stepinfo.
State Space
>> stepinfo(Gcl)
ans =
RiseTime: 0.1587
SettlingTime: 0.4420
SettlingMin: 0.9131
SettlingMax: 1.0410
Overshoot: 4.0996
Undershoot: 0
Peak: 1.0410
PeakTime: 0.3410

## Slide 147
Sensitivity
Section: 6
We may numerically investigate how the performance changes as we make small changes to the three controller gains. It transpires that small changes to the first and second gain (changing them to -280 and -7.8 for example) hardly affects the closed-loop step response at all (although of course Nbar must be recalculated). The sensitivity is to the third, smaller gain and indeed here again small percentage changes have relatively little affect. The real issue here is that the ratio of the largest to the smallest gain is rather big and that the task of realisation may present a problem.
State Space

## Slide 148
Observers
Section: 6
Full-state linear feedback assumes that all of the states can feasibly be measured. Luenberger proposed an ingenious alternative. Instead of measuring all of the states we measure the output only and build a system which is capable of estimating the remaining states. Such a system is called an observer.
State Space

## Slide 149
Observer
Section: 6
The state of the observer is employed as the estimate of the state of the plant and is fed back just as if it were in fact the correct state vector. The matrix L is chosen so that overall closed-loop system performance is acceptable.
State Space
where matrix K is also to be chosen for acceptable performance. K is chosen as above and before L.
Notes: Note: we assume that D = 0. We also assume that we have a perfect model of the system. This is clearly not the case.
Now it is perhaps plausible, if not obvious, that the state of the overall system comprises the concatenation of the states of the plant and the observer.

## Slide 150
The problem with observers
Section: 6
Of course there is a very obvious problem with this idea. We assume that not only does a perfect linear time-invariant model of the system exist, we assume also that we know it. The observer is designed quite explicitly in terms of the matrices A, B, C and D of the state-space realisation. One can argue in many ways why this is not so great a problem as it first appears, but in truth it is.
State Space

## Slide 151
Observer
Section: 6
Alternative state
The great value of this change of state is that the state transition matrix in the new formulation is block triangular. It is a basic property of matrices that the eigenvalues of this block triangular matrix are the union of the eigenvalues of A-BK and the eigenvalues of A-LC.
State Space
One possible state

## Slide 152
Observer Estimation Error
Section: 6
State Space
Focus on second half:
eobs is the difference between the actual state and the state estimate provided by the observer. The matrix A-LC describes the estimation error dynamics, but how?
The poles of the transfer function of a system are equal to the eigenvalues of the state transition matrix of a state space representation of the system. The system is stable if the poles are in the open LHP. It is finally time to start to engage with the state space equation.

## Slide 153
Stability
Section: 6
State Space
Consider the differential equation:
One of the most significant ideas in state space formulation (and indeed more generally in matrix theory) is the idea of changing the state, commonly called a change of basis. Let us introduce a new state vector
z = Mx for some non-singular matrix M.

## Slide 154
Stability
Section: 6
State Space
Now an excellent result of matrix theory says that for almost all matrices A there exists a matrix M (not necessarily real) such that the associated matrix MAM-1 is diagonal. Assume for simplicity that M can be and has been chosen to achieve this diagonalisation.
Notes: For this choice of state the system is seen to correspond to a collection of decoupled first order equations.
Now a form of stability for a linear, time-invariant system (global asymptotic stability in the sense of Lyapunov) roughly requires that, irrespective of the initial condition, the state of the system should remain bounded and converge to zero.
Evidently each component will remain bounded and converge to zero irrespective of the initial condition if and only if the numbers lambda_i (which may be complex) have negative real part, i.e. lie in the open LHP. It is also fairly clear that if z is bounded and converges to zero then x behaves likewise. Accordingly the dynamical system is said to be stable in this case if the diagonal elements of the diagonal matrix lie in the open LHP. The use of the word “stable” is careless and vague in this case, but it is also very common.

## Slide 155
Stability
Section: 6
State Space
We see that for this special choice of basis (or definition of state) the equations decouple. The system actually ends up looking like a whole collection of first order systems. This observation lies at the very heart of the techniques commonly referred to either as modal analysis or Fourier analysis. Now a form of stability for a linear, time-invariant system (global asymptotic stability in the sense of Lyapunov) roughly requires that, irrespective of the initial condition, the state of the system should remain bounded and converge to zero. Evidently each component will remain bounded and converge to zero irrespective of the initial condition if and only if the numbers li (which may be complex) have negative real part, i.e. lie in the open LHP. It is also fairly clear that if z is bounded and converges to zero then x behaves likewise. Accordingly the dynamical system is said to be stable in this case if the diagonal elements of the diagonal matrix lie in the open LHP. The use of the word “stable” is careless and vague in this case, but it is also very common.

## Slide 156
Stability
Section: 6
State Space
Two matrices A and B related to each other by B = MAM-1 for some non-singular matrix M are said to be similar. An important result of matrix theory is that two matrices are similar only if they have the same eigenvalues. A proof of this proposition goes as follows:
In the argument above matrices A and L are similar and therefore have equal eigenvalues. It is rather trivial that the eigenvalues of a diagonal matrix are its diagonal elements. Accordingly the numbers li above are the eigenvalues of L and are therefore also the eigenvalues of A.

## Slide 157
Stability
Section: 6
State Space
Condition for stability: Dynamical system
is stable if and only if the eigenvalues of matrix A lie in the open LHP. Moreover, if (S1) is stable then the state x remains bounded and converges to zero irrespective of the initial state. The latter is loosely the definition of global asymptotic stability in the sense of Lyapunov. Convergence is more rapid if the eigenvalues are further into the LHP.

## Slide 158
Observer Estimation Error
Section: 6
State Space
Returning to the observer error dynamics:
the estimation error eobs will converge to zero rapidly if the eigenvalues of the matrix A-LC are sufficiently far into the LHP. Of course this is exactly what we want if the observer is to provide an accurate estimate of the state of the plant. The choice of matrix L (which is sometimes called the observer gain) becomes a standard pole-placement problem. We look to place the eigenvalues of A-LC at -100, -101 and -102 (they must be distinct if we are to use the place command).

## Slide 159
Observer Estimation Error
Section: 6
State Space
The eigenvalues of a matrix equal those of its transpose. Accordingly we seek to place the eigenvalues of AT-CTLT.
A minor problem is that place finds K in A-BK to achieve certain poles whereas here we need to find L in A-LC to achieve the same result. In the former the unknown is pre-multiplied by B and in the latter it is post-multiplied by C.
= [203 11282 0]
>> L = place(A',C',[-100 -101 -102])';

## Slide 160
Finally include Nbar
Section: 6
State Space

## Slide 161
Finally include Nbar
Section: 6
State Space
We require that DC gain of closed loop system equals unity:

## Slide 162
Note on Matlab
Section: 6
State Space
>> K= place(A,B,[-3 -4])
>> Nbar = -1/(C*inv(A-(B*K))*B)
>> L = place(A',C',[-20 -21])'

## Slide 163
Note on Matlab
Section: 6
State Space
>> Acl = [A-(B*K) B*K; zeros(size(A)) A-(L*C)]
>> Bcl = Nbar*[B;zeros(length(A),1)]
>> Ccl = [C zeros(1,length(A)], Dcl = D

## Slide 164
Note on Matlab
Section: 6
State Space
But answer is
>> [Numcl,Dencl] = ss2tf(Acl,Bcl,Ccl,Dcl]
>> Gcl = tf(Numcl,Dencl)

## Slide 165
Note on Matlab
Section: 6
State Space
So the answer given by Matlab is correct, but is not in reduced form, i.e. there are common zeros and poles which can be cancelled. This impacts on the evaluation of the zeros of the resulting closed loop transfer function. Matlab will report the zeros as being the actual zero -1 as well as the roots of the polynomial s2+41s+420 which are -20 and -21, i.e. the chosen poles of the error dynamics.

## Slide 166
Pole Placement
Section: 6
State Space
We seek matrix K such that the eigenvalues of A-BK lie at specified locations. Software such as Matlab’s place command achieves this, but how? Consider the special case of a single input system, i.e. B is nx1 and K is 1xn. The key observation is that the problem is very simple to solve if matrices A and B have a particular form:
The matrix A is said to be in companion form.

## Slide 167
Companion form
Section: 6
State Space

## Slide 168
Example 6.2
Section: 6
State Space
eig(A) =
-7.4361
-0.2819 + 0.8529i
-0.2819 - 0.8529i

## Slide 169
State Space Transformation
Section: 6
State Space
Introduce a new state vector z = Mx for some
non-singular matrix M.
The new representation has the standard state space model form but in place of the matrices (A,B,C,D) we have new matrices (MAM-1, MB, CM-1, D). Notwithstanding the new matrices we claim that this is actually the same system.

## Slide 170
State Space Transformation
Section: 6
State Space
One way in which we can mathematically establish this equivalence is to determine the transfer function matrix for the new description:
That is to say, the transfer function matrix is unchanged by the change of basis, reflecting that the system itself is unchanged by our decision as to how to describe it.

## Slide 171
Pole Placement
Section: 6
State Space
The pole placement procedure above can now be applied if the matrices MAM-1 and MB have the special form required.
The issue becomes a purely matrix theoretical question: under what conditions on matrices A and B (the latter being nx1) will there exist a non-singular matrix M such that matrix MAM-1 is in companion form and matrix MB is equal to the special column vector en ?

## Slide 172
Controllable Canonical Form
Section: 6
State Space
for some row vector qT yet to be chosen.
By an important result from matrix theory called the Cayley-Hamilton theorem

## Slide 173
Controllable Canonical Form
Section: 6
State Space

## Slide 174
Controllable Canonical Form
Section: 6
State Space
is called the controllability matrix which we assume non-singular.

## Slide 175
Complete Controllability
Section: 6
State Space
The matrix pair (A,B) (the latter being assumed to be a column vector) will be said to be completely controllable if the associated controllability matrix G is non-singular.
The system will be said to be completely controllable if in any state space realisation (A,B,C,D) the matrix pair (A,B) is completely controllable.
If the system is completely controllable relative to the state space realisation (A,B,C,D) then it is completely controllable relative to any equivalent state space realisation (MAM-1 , MB, CM-1 , D).

## Slide 176
Controllable Canonical Form
Section: 6
State Space
Matrices A and B can be transformed to form required for application of the simple pole-placement procedure provided the matrix pair (A,B) is completely controllable. The special form that the state space model takes when matrix A is in companion form and matrix B equals en is called controllable canonical form because, as outlined above, any realisation of a completely controllable system can be transformed to a realisation having this form.
So to solve the pole-placement problem for a single input system: transform to controllable canonical form, apply the simple pole-placement procedure for a system in this form and then transform back.

## Slide 177
Let us apply this procedure to the ball and field problem:
Section: 6
State Space
Example 6.3
Current characteristic poly:

## Slide 178
Example 6.3
Section: 6
State Space
Transform to controllable canonical form

## Slide 179
Example 6.3
Section: 6
State Space
Apply special pole-placement method to transformed system
Notes: Confirm with eig(A-BK).

## Slide 180
Controllability and Observability
Section: 6
State Space
In pole-placement, with or without the observer, the
mathematical problem of selecting matrix K such that the
eigenvalues of matrix A-BK should take on certain desirable
values arose. This problem is not always solvable. Suppose:
eigenvalues:

## Slide 181
Example 6.4
Section: 6
Steady State
The first and second components (x1 and x2) of the state vector are totally unaffected by the input signal e. Kalman says that the individual states x1 and x2 are uncontrollable.
The third state x3 can be driven from any initial value to any desired final value in any prescribed time-interval. Kalman says that this state is controllable.

## Slide 182
Controllability
Section: 6
State Space
When the matrix A is diagonal it is simple in general to determine which states are controllable and which are uncontrollable. A state is controllable if the corresponding row of matrix B is non-zero and uncontrollable if this row is zero. A system is completely controllable if all of the states are controllable.
Kalman acquires a necessary and sufficient condition for a system to be completely controllable.
The controllability matrix G , defined above, should have rank n (which is the same as being non-singular in the single input case).
If the controllability matrix for any realisation (A,B,C,D) is non-singular then the controllability matrix for any equivalent realisation (MAM-1,MB,CM-1,D) is also non-singular so that Kalman’s condition is independent of the particular realisation being used, i.e. it is a property of the system not of the realisation.

## Slide 183
Example 6.4
Section: 6
State Space
If we consider the transfer function of the system above we obtain:
and we see that a pole-zero cancellation occurs reducing the transfer function to

## Slide 184
Controllability
Section: 6
State Space
We saw above that the complete controllability condition is necessary and sufficient for the realisation of a system to be transformable to a realisation in controllable canonical form, i.e. with state transition matrix in companion form and vector MB equal to the special unit vector en . Accordingly a system is completely controllable if and only if it has a realisation in controllable canonical form.
Moreover, for a system with a single input the pole-placement problem can always be solved if and only if the system is completely controllable.

## Slide 185
Controllability
Section: 6
State Space
A nasty scenario is where one has an unstable uncontrollable mode or state. What will happen here? At some point a perturbation or disturbance will evoke the mode, putting some energy into it. The corresponding state will now start to grow without bound. Moreover, at least according to the linear theory, there is no possible control action which can put this right. The instability cannot be mitigated.

## Slide 186
Controllability and Observability
Section: 6
State Space
In pole-placement with the observer, the mathematical
problem of selecting matrix L such that the eigenvalues of
matrix A-LC should take on certain desirable
values arose. This problem is not always solvable. Suppose:
eigenvalues:

## Slide 187
Example 6.5
Section: 6
Steady State
Components x1 and x2 have no influence on the output signal y. Kalman says that the states x1 and x2 are unobservable. The third state x3 does affect the output and can be determined at any time tf if the input and output are known over the time interval [0,tf]. Kalman says that this state is observable.

## Slide 188
Observability
Section: 6
State Space
When the matrix A is diagonal it is simple in general to determine which states are observable and which are unobservable. A state is observable if the corresponding column of matrix C is non-zero and unobservable if this column is zero. A system is completely observable if all of the states are observable.
Kalman acquires a necessary and sufficient condition for a system to be completely observable. The observability matrix.
should have rank n (which is the same as being non-singular in the single output case). This is also a property of the system, not the realisation.

## Slide 189
Example 6.5
Section: 6
State Space
If we consider the transfer function of the system above we obtain:
and we see that a pole-zero cancellation occurs reducing the transfer function to

## Slide 190
Observability
Section: 6
State Space
Now the problem of selecting matrix L to place the eigenvalues of A-LC is equivalent to the problem of selecting matrix LT such that the eigenvalues of matrix AT-CTLT should take on certain values. But this is just the standard pole-placement problem applied to the matrix pair (AT , CT) with a new notation LT for the solution. Accordingly this problem can be solved in general if and only if the matrix pair (AT , CT) is completely controllable. Note that the matrix pair (A,C) is completely observable iff the matrix pair (AT , CT) is completely controllable. Accordingly the pole-placement problem for A-LC is solvable in general iff the system is completely observable.

## Slide 191
Observability
Section: 6
State Space
A nasty scenario is where one has an unstable unobservable mode or state. What will happen here? Well initially nothing. Viewed from the output the mode has no impact at all, it is unobservable. At some point however some perturbation or disturbance will evoke the mode, putting some energy into it. The corresponding state will now start to grow without bound. Initially this will still be unobservable at the output. But of course the system model is lying when it asserts that the system is linear. The system is not linear, it only looks linear when we operate close to certain desired values. The growing unobservable state pulls the system away from the operating point and suddenly, out of the blue, the system starts to behave very badly.

## Slide 192
Observability
Section: 6
State Space
A nightmare scenario is where one has an unstable, unobservable and uncontrollable mode or state. Now, not only is the system suddenly and without warning going to start to behave very badly, there is also nothing we can do about it.